## Slide 1
XiangShan V 扩展 Issue
1
统计、确认依据与真实 PoC
代码分类与 Mutation 建议
固定集合：89 个 Issue Issue 核查：2026-09-17，文档更新：2026-09-18
Notes: 来源：isla工作区原始89条Issue清单，以及对应GitHub原帖、标签和评论。

## Slide 2
Issue 集合概况
原始清单固定为 89 个 Issue，元数据按 GitHub 原帖校准
2
统计项 | 结果
Issue 总数 | 89
作者数 | 22
创建时间范围（UTC） | 2024-04-16 至 2026-09-16
当前 Open / Closed | 57 / 32
范围说明 | 包含 RTL、工具、重复、讨论与性能条目

## Slide 3
作者数量与发帖时间（1）
时间为该作者在本次 89 条集合中的最早和最晚创建日期（UTC）
3
作者 | Issue | Open | Closed | 创建日期范围
lhb-sec | 20 | 19 | 1 | 2026-05-25 至 2026-09-11
KnightGOKU | 14 | 10 | 4 | 2026-03-25 至 2026-05-10
wndmll643 | 8 | 6 | 2 | 2026-07-21 至 2026-09-16
youzi27 | 8 | 5 | 3 | 2025-11-29 至 2026-05-11
jimmymtest | 6 | 6 | 0 | 2026-04-20 至 2026-04-22
LeeHaofeng | 5 | 3 | 2 | 2026-06-07 至 2026-06-13
zhangkanqi | 5 | 3 | 2 | 2026-04-06 至 2026-04-08
camel-cdr | 4 | 0 | 4 | 2024-04-16 至 2025-01-16
cesarus777 | 3 | 0 | 3 | 2025-12-24 至 2025-12-24
nyh1 | 3 | 0 | 3 | 2026-05-28 至 2026-05-28
maplejty814 | 2 | 2 | 0 | 2026-06-26 至 2026-06-29

## Slide 4
作者数量与发帖时间（2）
时间为该作者在本次 89 条集合中的最早和最晚创建日期（UTC）
4
作者 | Issue | Open | Closed | 创建日期范围
0x1B05 | 1 | 1 | 0 | 2026-05-14 至 2026-05-14
biquanha | 1 | 0 | 1 | 2026-03-19 至 2026-03-19
cyyself | 1 | 0 | 1 | 2024-05-27 至 2024-05-27
H-Y-B | 1 | 0 | 1 | 2024-11-29 至 2024-11-29
Hoshi44 | 1 | 1 | 0 | 2026-04-05 至 2026-04-05
I3eg1nner | 1 | 0 | 1 | 2025-12-26 至 2025-12-26
jlong299 | 1 | 0 | 1 | 2024-12-10 至 2024-12-10
kds1123001 | 1 | 0 | 1 | 2026-08-24 至 2026-08-24
msuadOf | 1 | 0 | 1 | 2026-08-24 至 2026-08-24
Security-HC | 1 | 1 | 0 | 2026-06-26 至 2026-06-26
WaltJr-OH | 1 | 0 | 1 | 2025-03-06 至 2025-03-06

## Slide 5
Issue 创建时间分布
2026 年 75 条，2025 年 8 条，2024 年 6 条
5
Chart: 
| 03月 | 04月 | 05月 | 06月 | 07月 | 08月 | 09月
Issue数量 | 3 | 18 | 21 | 10 | 8 | 3 | 12
图中仅展示本次集合的 2026 年分布，不代表全仓库缺陷发生率。

## Slide 6
香山确认的判定口径
标签、最终评论、问题归属与修复证据分别记录
6
确认依据：明确的 confirmed / fixed 标签，或维护者对该问题的确认、修复说明。
归属另行判断：已确认问题可能属于 RTL、DiffTest、NEMU 或性能，不能合并统计。
Open / Closed 与修复分开：#6561、#6015 仍 Open，但评论已有修复记录。
WIP、reported 或“稍后检查”不构成确认。分支线索与混合历史问题单列。
Notes: 逐条证据见服务器 V扩展issue核验与PoC数据.json。

## Slide 7
89 条 Issue 的核验结果
7
归类 | 数量 | 说明
已确认 RTL / 调试 | 28 | 含 1 条重复映射 #6022
已确认工具问题 | 2 | #5279 DiffTest，#5426 NEMU
已确认性能问题 | 1 | #4190 的不必要依赖
行为对齐记录 | 1 | #5725，维护者说明非功能 Bug
部分确认 / 分支相关 | 2 | #2890、#6576，不能整帖直接计数
无效 / 非功能 / 重复等 | 27 | 含维护者否认、报告者撤回、历史记录
尚无充分确认依据 | 28 | 保留为待核查报告
合计 | 89 | 按 Issue 计数，不等于独立 Bug 数

## Slide 8
确认结论中的关键区别
8
#6467：reported / WIP 标签仍在，但维护者明确确认 deqPtr 更新 Bug，并指向 PR #6474。
#6168：维护者明确称为 known issue，属于调试触发器问题；原帖还没有完成可执行 PoC。
#5279 / #5426：分别属于 DiffTest 与 NEMU。#5725 属于保留行为的实现对齐。
#6039：现有 9 个本地 PoC 的关联 Issue，目前仍是待确认报告，不列入后面的已确认 RTL 主表。
Notes: 具体评论链接在89条明细页的备注与远程报告中。

## Slide 9
全量 Issue 清单（1/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
9
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6576 | 2026-09-16 | wndmll643 | Open | 部分确认 | vlse32.v 异常 mtval
#6561 | 2026-09-11 | lhb-sec | Open | 确认/修复 | vl=0 / VS Dirty
#6555 | 2026-09-11 | wndmll643 | Closed | 报告撤回 | vssubu.vx / vxsat
#6545 | 2026-09-10 | lhb-sec | Open | 待确认 | masked vsrl.vv 挂死
#6544 | 2026-09-10 | lhb-sec | Open | 待确认 | vcpop.m 非对齐组
#6543 | 2026-09-10 | lhb-sec | Open | 待确认 | vdiv.vx 除零挂死
#6540 | 2026-09-10 | wndmll643 | Open | 确认RTL | 向量/标量页错 stval
Notes: #6576 `mtval` is not written on a load access fault taken by a vector strided load (`vlse32.v`) — kunminghu-v3
https://github.com/OpenXiangShan/XiangShan/issues/6576
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6576", "label_snapshot": "module: memory, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6576#issuecomment-5692218398", "summary": "维护者认为v2由PR6548修复，v3计划移植；分支相关线索单列，不视为当前v3已完整确认/修复", "quote": "I think this issue has been fixed in `kunminghu-v2`. See PR https://github.com/OpenXiangShan/XiangShan/pull/6548.\nVector support for `kunminghu-v3` is still under development, and we'll apply the corresponding fixes to v3 in the future.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6561 Incorrect `mstatus.VS` Dirty update for `vl=0` vector memory instructions
https://github.com/OpenXiangShan/XiangShan/issues/6561
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6561", "label_snapshot": "type: bug/confirmed, module: backend, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6561#issuecomment-5661448507", "summary": "confirmed 标签；维护者说明已在 PR #6570 修复，报告者回测通过。", "quote": "If the value of the `vstart` register is 0, a `vector store` instruction will not alter the vector state and therefore will not generate a `DirtyVS`; if the value of the `vstart` register is not 0, all successfully executed vector instructions will reset `vstart` to `0` upon completion, thereby altering the vector state and generating a `DirtyVS`.\nI have fixed this in this PR. [https://github.com/OpenXiangShan/XiangShan/pull/6570](https://github.com/OpenXiangShan/XiangShan/pull/6570)\nI successfully ran the test cases locally.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6555 `vssubu.vx` (vector fixed-point unsigned saturating subtract) does not set `vxsat` when it saturates — kunminghu-v3
https://github.com/OpenXiangShan/XiangShan/issues/6555
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6555", "label_snapshot": "module: backend, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6555#issuecomment-5642683809", "summary": "报告者：implementation-defined behavior, not a bug，关闭Issue", "quote": "Thanks for your reply. While re-analyzing some other bug, I found out that this is an implementation-defined behavior, not a bug. Closing the issue.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6545 `vsrl.vv` with `v0.t` mask hangs and never writes back the destination register
https://github.com/OpenXiangShan/XiangShan/issues/6545
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6545", "label_snapshot": "module: backend, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6545", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6544 `vcpop.m` is incorrectly reported as an illegal instruction when `LMUL=8` and `vs2` is not group-aligned
https://github.com/OpenXiangShan/XiangShan/issues/6544
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6544", "label_snapshot": "module: backend, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6544", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6543 `vdiv.vx` with a zero divisor deadlocks the core
https://github.com/OpenXiangShan/XiangShan/issues/6543
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6543", "label_snapshot": "module: backend, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6543", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6540 `stval` mismatch on a scalar store **page** fault after a vector store **page** fault (S-mode) — kunminghu-v2
https://github.com/OpenXiangShan/XiangShan/issues/6540
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6540", "label_snapshot": "type: bug/confirmed, module: memory, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6540", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]

## Slide 10
全量 Issue 清单（2/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
10
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6536 | 2026-09-09 | lhb-sec | Open | 待确认 | vmadc.vi mask tail
#6486 | 2026-09-04 | wndmll643 | Open | 待确认 | vsseg2e16.v 数据
#6482 | 2026-09-04 | lhb-sec | Open | 确认RTL | 连续异常 mtval 陈旧
#6475 | 2026-09-03 | wndmll643 | Open | 待确认 | vsseg3e32.v uop 数
#6467 | 2026-09-02 | wndmll643 | Closed | 确认/修复 | StoreQueue 指针回绕
#6410 | 2026-08-24 | msuadOf | Closed | 无效报告 | move / merge 组对齐
#6407 | 2026-08-24 | kds1123001 | Closed | 无效报告 | 无效 VSEW 的 load
Notes: #6536 `vmadc.vi` zeroes mask-destination tail bits
https://github.com/OpenXiangShan/XiangShan/issues/6536
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6536", "label_snapshot": "module: backend, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6536", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6486 Legal segmented store `vsseg2e16.v` silently commits wrong store data (0 instead of the source value) — vector store-data unit emits 0 for a field on kunminghu-v3
https://github.com/OpenXiangShan/XiangShan/issues/6486
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6486", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6486", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6482 Stale mtval after consecutive same-direction RVV memory access faults
https://github.com/OpenXiangShan/XiangShan/issues/6482
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6482", "label_snapshot": "type: bug/confirmed, module: unknown, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6482", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#6475 Legal segmented store `vsseg3e32.v` triggers `robEntries uopNum is overflow!` (ROB uop-count underflow) — deterministic assertion abort on kunminghu-v3
https://github.com/OpenXiangShan/XiangShan/issues/6475
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6475", "label_snapshot": "type: bug/reported, module: backend, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6475", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6467 StoreQueue `deqPtr > rdataPtr` assertion fails at the physical-queue wrap boundary under vector stores
https://github.com/OpenXiangShan/XiangShan/issues/6467
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6467", "label_snapshot": "type: bug/reported, module: memory, module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6467#issuecomment-5522852062", "summary": "weidingliu：indeed a bug of deqPtr update；We fixed it in #6474", "quote": "1. That's indeed a bug of `deqPtr` update, and it's the first time to be observed.\n2. The asymmetric `dataQueue.io.empty` gate between the `deqPtr` (:1272) and `rdataPtr` (:1302) inactive skips is intentional. We fixed it in #6474", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6410 vmove-class instructions (vmv.v.*, vmerge.*) with misaligned register groups don't raise illegal instruction (test-matrix confirmed, extends #5772)
https://github.com/OpenXiangShan/XiangShan/issues/6410
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6410", "label_snapshot": "type: bug/invalid, module: backend, module: vector, type: bug/WIP feature"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6410", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6407 Vector load doesn't trigger illegal instruction trap when VSEW is invalid
https://github.com/OpenXiangShan/XiangShan/issues/6407
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6407", "label_snapshot": "type: bug/invalid, module: vector, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6407", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]

## Slide 11
全量 Issue 清单（3/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
11
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6399 | 2026-08-21 | lhb-sec | Open | 确认RTL | 连续 store fault mtval
#6302 | 2026-07-28 | lhb-sec | Open | 待确认 | reserved VSEW
#6298 | 2026-07-28 | lhb-sec | Open | 未实现 | vstart / 未实现指令
#6296 | 2026-07-28 | lhb-sec | Open | 待确认 | store fault mcause
#6295 | 2026-07-28 | lhb-sec | Open | 待确认 | FOF 目的寄存器
#6293 | 2026-07-28 | lhb-sec | Open | 待确认 | FOF / I/O PMA
#6292 | 2026-07-28 | wndmll643 | Open | 待确认 | 页错后的 vstart
Notes: #6399 `mtval` mismatch on scalar store access fault after a vector store access fault
https://github.com/OpenXiangShan/XiangShan/issues/6399
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6399", "label_snapshot": "type: bug/confirmed, module: backend, module: memory, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6399", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#6302 XiangShan does not trap on vector instruction with reserved vsew encoding
https://github.com/OpenXiangShan/XiangShan/issues/6302
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6302", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6302", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6298 XiangShan misses illegal-instruction trap for out-of-range vstart
https://github.com/OpenXiangShan/XiangShan/issues/6298
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6298", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6298#issuecomment-5542251829", "summary": "维护者明确unimplemented feature, not a bug", "quote": "I must claim that this issue just report a unimplemented feature, not a bug.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6296 Vector store reports wrong `mcause` in M-mode
https://github.com/OpenXiangShan/XiangShan/issues/6296
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6296", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6296", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6295 `vle32ff.v` corrupts destination vector register on Load Access Fault
https://github.com/OpenXiangShan/XiangShan/issues/6295
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6295", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6295", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6293 `vle64ff.v` misses Load Access Fault on misaligned access to I/O PMA region
https://github.com/OpenXiangShan/XiangShan/issues/6293
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6293", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6293", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6292 vstart set to wrong element on a page-faulting vector load (for debugging assistance)
https://github.com/OpenXiangShan/XiangShan/issues/6292
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6292", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6292", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]

## Slide 12
全量 Issue 清单（4/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
12
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6289 | 2026-07-27 | lhb-sec | Open | 待确认 | fault 后 AMO 活性
#6262 | 2026-07-21 | wndmll643 | Open | 待确认 | 未映射页 segment
#6168 | 2026-06-29 | maplejty814 | Open | 确认RTL | FOF watchpoint 丢失
#6152 | 2026-06-26 | Security-HC | Open | 待确认 | 扩展结果高位
#6151 | 2026-06-26 | maplejty814 | Open | 无效报告 | vl=0 segment 性能
#6093 | 2026-06-13 | LeeHaofeng | Closed | 无效报告 | 浮点冗余舍入代码
#6085 | 2026-06-11 | lhb-sec | Open | 待确认 | indexed store 提交
Notes: #6289 AMO deadlocks after `vse32.v` store access fault
https://github.com/OpenXiangShan/XiangShan/issues/6289
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6289", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6289", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6262 XS bug-report — vlseg to unmapped page deadlocks (VSegmentUnit)
https://github.com/OpenXiangShan/XiangShan/issues/6262
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6262", "label_snapshot": "module: vector, type: bug/WIP feature"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6262", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6168 [Bug] debug watchpoint trigger lost on FOF non-first element
https://github.com/OpenXiangShan/XiangShan/issues/6168
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6168", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6168#issuecomment-4913753242", "summary": "维护者确认known issue，计划后续修复", "quote": "This is a known issue. We are evaluating the specific matters for subsequent fixes. Thank you for your point.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6152 [RVV] vzext.vf4 / vsext.vf4 writes zero to high 64-bit (elements 2..3)
https://github.com/OpenXiangShan/XiangShan/issues/6152
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6152", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6152", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6151 [Performance] VSegmentUnit: segment instructions with vl=0 stall the memory unit hundreds of cycles instead of retiring immediately
https://github.com/OpenXiangShan/XiangShan/issues/6151
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6151", "label_snapshot": "type: bug/invalid, topic: performance, module: vector, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6151", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6093 ```VectorFloatAdder.scala``` overflow rounding uses wrong normal-path GRS bits
https://github.com/OpenXiangShan/XiangShan/issues/6093
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6093", "label_snapshot": "type: bug/invalid, module: vector"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6093", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6085 `vsoxei32.v` fails to commit store
https://github.com/OpenXiangShan/XiangShan/issues/6085
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6085", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6085", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]

## Slide 13
全量 Issue 清单（5/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
13
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6079 | 2026-06-10 | lhb-sec | Open | 待确认 | whole load 的 vstart
#6066 | 2026-06-07 | LeeHaofeng | Closed | 无效报告 | 废弃 VMask 模块
#6065 | 2026-06-07 | LeeHaofeng | Open | 待确认 | genVUopOffset 的 nf
#6064 | 2026-06-07 | LeeHaofeng | Open | 待确认 | VPermSrcType 条件
#6063 | 2026-06-07 | LeeHaofeng | Open | 明确非Bug | vfrec7 / fflags 格式
#6042 | 2026-05-29 | lhb-sec | Open | 待确认 | load fault 的 vstart
#6039 | 2026-05-28 | lhb-sec | Open | 待确认 | rd=x0 的 vsetvl 活性
Notes: #6079 `vl1re16.v` incorrectly computes `vstart` on Load Access Fault
https://github.com/OpenXiangShan/XiangShan/issues/6079
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6079", "label_snapshot": "module: vector, type: bug/WIP feature"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6079", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6066 VMask.scala ```shift``` truncation bug for ```SEW=8``` and large ```uopIdx```
https://github.com/OpenXiangShan/XiangShan/issues/6066
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6066", "label_snapshot": "type: bug/invalid, module: vector, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6066", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6065 ```genVUopOffset``` uses wrong ```nf``` semantics
https://github.com/OpenXiangShan/XiangShan/issues/6065
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6065", "label_snapshot": "type: bug/reported, module: vector, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6065", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6064 Copy-Paste Typo in Mux1H Default Condition — ```isvrgatherei16``` Repeated Instead of ```isvcompress``` in VPermSrcTypeModule
https://github.com/OpenXiangShan/XiangShan/issues/6064
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6064", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6064", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6063 ```CVT16.scala``` fflags ```NV``` lost for ```vfrec7 -inf```
https://github.com/OpenXiangShan/XiangShan/issues/6063
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6063", "label_snapshot": "type: bug/reported, module: vector, version: kunminghu-v3"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6063#issuecomment-4678966210", "summary": "维护者说明fflags截断结果正确，仅代码格式问题，非功能bug", "quote": "Here `fflags0` is `5` bits, and the result after `Cat` is truncated to exactly `0`, so although it looks wrong, the result is correct.\nWe will fix the formatting issue in the `kunminghu-v3` branch later.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6042 `vle16.v` fault handling incorrectly sets `vstart` to `vl` instead of the faulting element index
https://github.com/OpenXiangShan/XiangShan/issues/6042
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6042", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6042", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6039 `vsetvl` with `rd=zero` causes core hang
https://github.com/OpenXiangShan/XiangShan/issues/6039
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6039", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6039", "summary": "只有 reported；维护者回复尚未 review/fix，不能视作确认。"}]

## Slide 14
全量 Issue 清单（6/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
14
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6037 | 2026-05-28 | nyh1 | Closed | 无效报告 | vmvnr 寄存器对齐
#6036 | 2026-05-28 | nyh1 | Closed | 无效报告 | vmv1r / vstart
#6035 | 2026-05-28 | lhb-sec | Open | 待确认 | FOF 异常 CSR
#6034 | 2026-05-28 | nyh1 | Closed | 明确非Bug | vfsgnj / FS Dirty
#6022 | 2026-05-25 | lhb-sec | Closed | 确认/重复 | 向量 load 挂死重复
#6015 | 2026-05-25 | lhb-sec | Open | 确认/修复 | indexed load 未映射
#5958 | 2026-05-14 | 0x1B05 | Open | 待确认 | 跨页 / replay assertion
Notes: #6037 [Bug] vmvnr_unaligned_regs
https://github.com/OpenXiangShan/XiangShan/issues/6037
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6037", "label_snapshot": "type: bug/invalid, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6037", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6036 [Bug] vmv1r_vstart_ge_evl
https://github.com/OpenXiangShan/XiangShan/issues/6036
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6036", "label_snapshot": "type: bug/invalid, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6036", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6035 `vle32ff.v` fails to update exception CSRs upon Load Access Fault
https://github.com/OpenXiangShan/XiangShan/issues/6035
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6035", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6035", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6034 【BUG】 `vfsgnj.vv` incorrectly dirties `mstatus.FS`
https://github.com/OpenXiangShan/XiangShan/issues/6034
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6034", "label_snapshot": "type: bug/reported, module: backend"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6034#issuecomment-4570036662", "summary": "sinceforYy：We do not believe this is a bug；fflags功能正确", "quote": "We do not believe this is a bug.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6022 `vlse64.v` fails to trigger Load Access Fault upon illegal address access
https://github.com/OpenXiangShan/XiangShan/issues/6022
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6022", "label_snapshot": "type: bug/confirmed, note: duplicate, module: memory"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6022#issuecomment-4539692989", "summary": "confirmed 标签；维护者称已由 PR #6020 修复的 vec-load hang，作为 #6015 同根因映射，不独计根因。", "quote": "This is a known issue caused by a vec load hang; we have already fixed it.https://github.com/OpenXiangShan/XiangShan/pull/6020", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6015 Pipeline hangs on `vluxei32.v` when accessing unmapped physical addresses
https://github.com/OpenXiangShan/XiangShan/issues/6015
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6015", "label_snapshot": "type: bug/confirmed, module: memory"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6015#issuecomment-4539489076", "summary": "维护者可复现并称 \"indeed a bug\"，后称已由 PR #6020 修复。", "quote": "Thank you for your report! That's indeed a bug caused by `d38fc34`, we will fix it later!", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5958 Kunminghu-v2: LoadQueueReplay assertion on translated cross-page vector byte load/store
https://github.com/OpenXiangShan/XiangShan/issues/5958
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5958", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5958", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]

## Slide 15
全量 Issue 清单（7/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
15
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5943 | 2026-05-11 | youzi27 | Open | 确认RTL | vsse16.v 的 mtval
#5934 | 2026-05-10 | KnightGOKU | Open | 确认RTL | masked segment 数据
#5933 | 2026-05-10 | KnightGOKU | Open | 确认RTL | zero-stride segment
#5932 | 2026-05-10 | KnightGOKU | Open | 确认RTL | indexed segment 数据
#5931 | 2026-05-10 | KnightGOKU | Open | 确认RTL | misaligned FOF field
#5930 | 2026-05-10 | KnightGOKU | Open | 确认RTL | FOF active byte
#5929 | 2026-05-10 | KnightGOKU | Closed | 无效报告 | 参考模型内存大小
Notes: #5943 Incorrect `mtval` for faulting `vsse16.v` on kunminghu-v2
https://github.com/OpenXiangShan/XiangShan/issues/5943
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5943", "label_snapshot": "type: bug/confirmed, module: unknown, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5943#issuecomment-4437990329", "summary": "confirmed 标签；维护者最终复现并明确 \"I think this issue is a bug\"。", "quote": "@youzi27 Ah ha, I finally reproduce this issue, I think this issue is a bug, which was introduced by (https://github.com/OpenXiangShan/XiangShan/commit/2bec9bddf90fa1ddd2690f344ef3f34e4346bb9e#diff-6db620258edc695befb5c4de9a76e239e89ff74d881e35a4ab978f931efb21aeR119) .", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5934 `vlseg2e16.v` corrupts an active destination lane during masked segment load
https://github.com/OpenXiangShan/XiangShan/issues/5934
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5934", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5934", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5933 `vlsseg3e64.v` loads wrong active destination data for zero-stride segment load
https://github.com/OpenXiangShan/XiangShan/issues/5933
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5933", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5933", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5932 `vluxseg5ei32.v` corrupts active destination data for indexed segment load
https://github.com/OpenXiangShan/XiangShan/issues/5932
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5932", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5932", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5931 `vlseg2e32ff.v` loads wrong field0 data for misaligned fault-only-first segment load
https://github.com/OpenXiangShan/XiangShan/issues/5931
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5931", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5931", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5930 `vle8ff.v` corrupts active loaded byte value
https://github.com/OpenXiangShan/XiangShan/issues/5930
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5930", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5930", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5929 `vloxseg5ei64.v` misses load access fault and commits destination vector registers
https://github.com/OpenXiangShan/XiangShan/issues/5929
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5929", "label_snapshot": "type: bug/invalid"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5929", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]

## Slide 16
全量 Issue 清单（8/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
16
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5928 | 2026-05-09 | youzi27 | Open | 确认RTL | vsext 元素选取
#5927 | 2026-05-09 | youzi27 | Closed | 自报重复 | vmv.x.s 重复报告
#5922 | 2026-05-09 | youzi27 | Closed | 自报重复 | frm 重复报告
#5921 | 2026-05-09 | youzi27 | Open | 待确认 | indexed store vstart
#5919 | 2026-05-08 | youzi27 | Open | 待确认 | reserved vmv<nr>r
#5865 | 2026-04-27 | KnightGOKU | Open | 确认RTL | vmerge 的 vd=v0
#5845 | 2026-04-22 | jimmymtest | Open | 待确认 | 三指令流水 assertion
Notes: #5928 Incorrect source element selection in `vsext`
https://github.com/OpenXiangShan/XiangShan/issues/5928
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5928", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5928", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5927 Incorrect scalar result from `vmv.x.s` when SEW is smaller than XLEN
https://github.com/OpenXiangShan/XiangShan/issues/5927
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5927", "label_snapshot": "note: duplicate"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5927#issuecomment-4412737115", "summary": "youzi27：This issue seems similar to #5829", "quote": "This issue seems similar to #5829 , so I will close it. Sorry for the confusion.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5922 Incorrect handling of invalid `frm` for `vfmerge.vfm`
https://github.com/OpenXiangShan/XiangShan/issues/5922
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5922", "label_snapshot": "note: duplicate"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5922#issuecomment-4411727439", "summary": "youzi27：This issue seems similar to #5768", "quote": "This issue seems similar to #5768 , so I will close it. Sorry for the confusion.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5921 Incorrect `vstart` update after faulting vector indexed store
https://github.com/OpenXiangShan/XiangShan/issues/5921
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5921", "label_snapshot": "module: memory, module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5921", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#5919 Reserved `vmv<nr>r.v` encodings are executed instead of being rejected
https://github.com/OpenXiangShan/XiangShan/issues/5919
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5919", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5919", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#5865 XiangShan misses illegal-instruction trap for reserved masked `vmerge.vvm` with vd = v0
https://github.com/OpenXiangShan/XiangShan/issues/5865
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5865", "label_snapshot": "type: bug/confirmed, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5865", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5845 [Assertion Failure] XiangShan crashes in `LoadUnitS0` on a reduced `vmsbf.m -> vl1re64.v -> vlseg4e8.v` sequence
https://github.com/OpenXiangShan/XiangShan/issues/5845
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5845", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5845", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]

## Slide 17
全量 Issue 清单（9/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
17
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5840 | 2026-04-22 | jimmymtest | Open | 确认RTL | vzext.vf8 零扩展
#5832 | 2026-04-20 | jimmymtest | Open | 确认RTL | whole load 高位截断
#5831 | 2026-04-20 | jimmymtest | Open | 确认RTL | mixed-EEW strided
#5830 | 2026-04-20 | jimmymtest | Open | 确认RTL | vfmv.f.s NaN-box
#5829 | 2026-04-20 | jimmymtest | Open | 确认RTL | vmv.x.s 符号扩展
#5809 | 2026-04-14 | KnightGOKU | Closed | 确认/修复 | vill 后 vmv.x.s
#5808 | 2026-04-14 | KnightGOKU | Open | 待确认 | vsse16.v 的 vstart
Notes: #5840 [BUG] `vzext.vf8` can compute the wrong zero-extended result for an active destination element.
https://github.com/OpenXiangShan/XiangShan/issues/5840
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5840", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5840", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5832 [BUG] `vl8re64.v` truncates upper 64-bit data in whole-register loads
https://github.com/OpenXiangShan/XiangShan/issues/5832
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5832", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5832", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5831 [BUG] `vlse32.v` corrupts packed 32-bit element data under SEW=64, LMUL=8 mixed-EEW execution
https://github.com/OpenXiangShan/XiangShan/issues/5831
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5831", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5831", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5830 [BUG] `vfmv.f.s` fails to NaN-box 32-bit values when writing to a 64-bit floating-point registe
https://github.com/OpenXiangShan/XiangShan/issues/5830
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5830", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5830", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5829 [Bug] vmv.x.s instruction fails to sign-extend when SEW < XLEN
https://github.com/OpenXiangShan/XiangShan/issues/5829
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5829", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5829", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5809 `vmv.x.s` executes instead of raising illegal-instruction when `vsetvli` leaves `vtype.vill=1`
https://github.com/OpenXiangShan/XiangShan/issues/5809
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5809", "label_snapshot": "module: backend, type: bug/fixed"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5809", "summary": "GitHub `type: bug/fixed` 标签；无 tool 标签，按 XiangShan 已确认且已有修复标签记录。"}]
#5808 `vstart` mismatch after a minimal `vsse16.v` RVV testcase
https://github.com/OpenXiangShan/XiangShan/issues/5808
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5808", "label_snapshot": "module: vector, type: bug/WIP feature"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5808", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]

## Slide 18
全量 Issue 清单（10/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
18
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5790 | 2026-04-08 | zhangkanqi | Closed | 无效报告 | 模型配置/自修改
#5777 | 2026-04-07 | zhangkanqi | Closed | 无效报告 | MinimalConfig 活性
#5772 | 2026-04-06 | zhangkanqi | Open | 确认RTL | vmv4r.v 组对齐
#5770 | 2026-04-06 | zhangkanqi | Open | 待确认 | 异常时部分写回
#5769 | 2026-04-06 | zhangkanqi | Open | 待确认 | indexed store mtval
#5768 | 2026-04-05 | Hoshi44 | Open | 确认RTL | FP move / merge frm
#5767 | 2026-04-05 | KnightGOKU | Open | 确认RTL | segment FOF 内部异常
Notes: #5790 Mismatch mcause and mtval when executing vssseg3e16.v
https://github.com/OpenXiangShan/XiangShan/issues/5790
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5790", "label_snapshot": "type: bug/invalid"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5790", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5777 No instructions have been submitted for a long time. Could this be a case of deadlock?
https://github.com/OpenXiangShan/XiangShan/issues/5777
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5777", "label_snapshot": "type: bug/invalid"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5777", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5772 vmv4r.v with misaligned registers dosen't raise illegal instruction exception
https://github.com/OpenXiangShan/XiangShan/issues/5772
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5772", "label_snapshot": "type: bug/confirmed, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5772", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5770 Vector whole register load(vl2re32.v) partially updates destination on exception
https://github.com/OpenXiangShan/XiangShan/issues/5770
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5770", "label_snapshot": "module: backend, module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5770", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#5769 Vector indexed segment store (vsuxseg*ei*) reports only base address in mtval on exception
https://github.com/OpenXiangShan/XiangShan/issues/5769
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5769", "label_snapshot": "module: backend, module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5769", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#5768 Vector FP move/merge instructions missing `frm` reserved value check
https://github.com/OpenXiangShan/XiangShan/issues/5768
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5768", "label_snapshot": "type: bug/confirmed, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5768", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5767 `vlseg2e8ff.v` with later-element fault triggers XiangShan internal critical error
https://github.com/OpenXiangShan/XiangShan/issues/5767
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5767", "label_snapshot": "type: bug/confirmed, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5767", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]

## Slide 19
全量 Issue 清单（11/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
19
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5766 | 2026-04-05 | KnightGOKU | Open | 确认RTL | FOF 后立即读 vl
#5765 | 2026-04-03 | KnightGOKU | Open | 确认RTL | vlm.v mask tail
#5739 | 2026-03-29 | KnightGOKU | Closed | 确认/修复 | vsetvli 后立即读 vl
#5725 | 2026-03-25 | KnightGOKU | Closed | 行为对齐 | reserved vsetvl 对齐
#5702 | 2026-03-19 | biquanha | Closed | 无效报告 | 无效向量访存报告
#5449 | 2025-12-26 | I3eg1nner | Closed | 无效报告 | VectorFloatFMA 对齐
#5426 | 2025-12-24 | cesarus777 | Closed | 确认工具 | NEMU vfredusum
Notes: #5766 `vle8ff` fault-only-first followed by immediate `csrr vl` returns 0 on XiangShan, while Spike returns the expected `vl`
https://github.com/OpenXiangShan/XiangShan/issues/5766
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5766", "label_snapshot": "type: bug/confirmed, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5766", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5765 Difftest mismatch on tail bits of v0 after vlm.v
https://github.com/OpenXiangShan/XiangShan/issues/5765
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5765", "label_snapshot": "type: bug/confirmed, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5765", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5739 `csrr vl` reads stale zero immediately after `vsetvli`
https://github.com/OpenXiangShan/XiangShan/issues/5739
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5739", "label_snapshot": "module: backend, type: bug/fixed"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5739", "summary": "GitHub `type: bug/fixed` 标签；无 tool 标签，按 XiangShan 已确认且已有修复标签记录。"}]
#5725 Behavior mismatch on RVV testcase (`vsetvl x0, x0, rs2` path)
https://github.com/OpenXiangShan/XiangShan/issues/5725
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5725", "label_snapshot": "module: backend, module: tool, type: bug/fixed"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5725#issuecomment-4132725504", "summary": "维护者 huxuan0307 明确 \"not a bug but a feature\"；后来 NEMU 与 XiangShan 统一对 reserved 情形报非法。", "quote": "Thank you for your bug report. As described in the vector section of the specification, the vsetvl[i] instruction is reserved when rs1 = x0 and rd = x0. Since there is no explicit description of how to implement reserved, the hardware can implement it in any reasonable way. In other words, this is not a bug but a \"feature\".", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5702 Vector memory access
https://github.com/OpenXiangShan/XiangShan/issues/5702
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5702", "label_snapshot": "type: bug/invalid, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5702", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5449 VectorFloatFMA module operation alignment logic error
https://github.com/OpenXiangShan/XiangShan/issues/5449
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5449", "label_snapshot": "type: bug/invalid"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5449", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5426 v31_low different on vfredusum.vs
https://github.com/OpenXiangShan/XiangShan/issues/5426
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5426", "label_snapshot": "module: tool, type: bug/fixed"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5426#issuecomment-3692247360", "summary": "维护者 lewislzh 明确 NEMU bug、\"RTL implementation is correct\"。", "quote": "Thanks for the issue report. This is indeed a bug in the NEMU simulator (the RTL implementation is correct)：\nThe RISC-V Vector specification states that for the vfredusum instruction, when an operand is masked off, it may be treated as -0 if the rounding mode is not RDN; for RDN, the operand needs to be treated as +0. NEMU’s handling of the RDN case was incorrect. A fix has been submitted.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]

## Slide 20
全量 Issue 清单（12/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
20
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5425 | 2025-12-24 | cesarus777 | Closed | 无效报告 | indexed store assertion
#5424 | 2025-12-24 | cesarus777 | Closed | 工具重复 | DiffTest 重复映射
#5288 | 2025-12-01 | youzi27 | Closed | 无效报告 | 自修改覆盖 fence.i
#5279 | 2025-11-29 | youzi27 | Open | 确认工具 | DiffTest store commit
#4368 | 2025-03-06 | WaltJr-OH | Closed | 讨论/建议 | VLEN 配置讨论
#4190 | 2025-01-16 | camel-cdr | Closed | 确认性能 | 向量吞吐/假依赖
#4017 | 2024-12-10 | jlong299 | Closed | 讨论/建议 | store-load 检查讨论
Notes: #5425 Assertion failed at DCache on vector indexed segment store instructions
https://github.com/OpenXiangShan/XiangShan/issues/5425
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5425", "label_snapshot": "type: bug/invalid, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5425", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5424 Mismatch for store commits on vector indexed segment store instructions
https://github.com/OpenXiangShan/XiangShan/issues/5424
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5424", "label_snapshot": "note: duplicate, module: tool"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5424#issuecomment-3689978534", "summary": "Yan-Muzi：Please refer to #5279", "quote": "Please refer to #5279.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5288 Unexpected interaction between vs1r.v and fence.i instructions
https://github.com/OpenXiangShan/XiangShan/issues/5288
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5288", "label_snapshot": "type: bug/invalid, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5288", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5279 Mismatch in vector store commit behavior under misaligned base address
https://github.com/OpenXiangShan/XiangShan/issues/5279
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5279", "label_snapshot": "type: bug/confirmed, module: tool"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5279#issuecomment-3595092909", "summary": "维护者 Yan-Muzi 明确：\"known bug of difftest\"，非 RTL。", "quote": "It is a known bug of difftest. We have not really figured out how to compare store commits of vector stores. We may fix this in the future.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#4368 Vector Configuration
https://github.com/OpenXiangShan/XiangShan/issues/4368
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4368", "label_snapshot": "type: question/answered"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4368", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#4190 KunminghuV2Config doesn't seem to dual issue vector instructions
https://github.com/OpenXiangShan/XiangShan/issues/4190
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4190", "label_snapshot": "type: bug/reported"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4190#issuecomment-2597589506", "summary": "维护者确认不必要vd依赖性能问题，PR4198修复且报告者回测；LMUL1解码限制另属设计取舍", "quote": "The above issue has been fixed by https://github.com/OpenXiangShan/XiangShan/pull/4198", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#4017 Store-load violation checking for vector instruction
https://github.com/OpenXiangShan/XiangShan/issues/4017
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4017", "label_snapshot": "type: question/answered"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4017", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]

## Slide 21
全量 Issue 清单（13/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
21
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#3962 | 2024-11-29 | H-Y-B | Closed | 讨论/建议 | 关闭 V 扩展配置
#3488 | 2024-09-03 | camel-cdr | Closed | 讨论/建议 | vcompress 优化建议
#3200 | 2024-07-14 | camel-cdr | Closed | 讨论/建议 | RVV benchmark 性能
#3012 | 2024-05-27 | cyyself | Closed | 工具历史 | NEMU 历史修复
#2890 | 2024-04-16 | camel-cdr | Closed | 部分确认 | 长程序/多问题历史
Notes: #3962 How to turn off vector instruction extension？
https://github.com/OpenXiangShan/XiangShan/issues/3962
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3962", "label_snapshot": "type: question/answered"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3962", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#3488 Why does only one execution unit support vppu? & vcompress optimization suggestion
https://github.com/OpenXiangShan/XiangShan/issues/3488
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3488", "label_snapshot": "type: question/answered"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3488", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#3200 rvv-bench: XiangShan performance problems
https://github.com/OpenXiangShan/XiangShan/issues/3200
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3200", "label_snapshot": "type: problem/answered"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3200", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#3012 Difftest failed on a RISC-V Vector memcpy workload with misaligned(in vlen granularity, not element) unit stride load
https://github.com/OpenXiangShan/XiangShan/issues/3012
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3012", "label_snapshot": "type: bug/reported"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3012#issuecomment-2134233149", "summary": "作者cyyself：Fixed NEMU commit b9796f4ec8b8427b4fb995ec948ed345f1caeaf4", "quote": "Fixed [https://github.com/OpenXiangShan/NEMU/commit/b9796f4ec8b8427b4fb995ec948ed345f1caeaf4](https://github.com/OpenXiangShan/NEMU/commit/b9796f4ec8b8427b4fb995ec948ed345f1caeaf4) .", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#2890 Simulation hangs for longer running functions using the vector extension
https://github.com/OpenXiangShan/XiangShan/issues/2890
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/2890", "label_snapshot": "type: bug/reported"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/2890#issuecomment-2220740793", "summary": "维护者给出RTL修复PR3140/commit1a0c5d且报告者验证；同帖后续还有nexus-am与VS配置问题，不整帖算单一RTL缺陷", "quote": "We have fixed the issue at this commit(1a0c5d77fed8b13a9fa5f70d1f25d808a311dd7b) in this pull requests (https://github.com/OpenXiangShan/XiangShan/pull/3140). This will later be integrated into the master.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]

## Slide 22
文档归纳的四种固定模板
22
模板 | 代表 Issue | 程序结构
KnightGOKU 手写最小复现 | #5739 / #5765 / #5766 / #5767 | trap handler、VS、目标序列、结果落盘
jimmymtest 自校验 | #5829 至 #5840 | FS/VS、gp 比较、tohost、通用 handler
riscv-tests env-p | #6576 | 标准复位框架、PMP、降权执行
fuzzer 运行时 | #5772 / #6399 / #6561 | 固定运行时、随机指令流、差分筛选
Notes: 来源：XiangShan-V扩展issue与PoC提取.md，第三部分。

## Slide 23
模板 1：PMP 边界与目标序列
#5766，M 模式手写最小复现骨架节选
23
la t0, deny_start
srli t0, t0, 2
csrw pmpaddr0, t0
la t1, deny_end
srli t1, t1, 2
csrw pmpaddr1, t1
li t2, 0x8800
csrw pmpcfg0, t2
li a0, 8
vsetvli t3, a0, e8, m1, tu, mu
vmv.v.i v8, 0
la a1, deny_start
addi a1, a1, -7
vle8ff.v v8, (a1)
csrr t4, vl
TOR 划定 deny 区，L 位使 M 模式也受约束。
地址偏移 -7 控制第 8 个字节触发 fault。
文档代码节选；GitHub Issue #5766
Notes: 来源：XiangShan-V扩展issue与PoC提取.md
https://github.com/OpenXiangShan/XiangShan/issues/5766

## Slide 24
模板 1：ebreak 出口与结果落盘
#5766，正常结束和意外异常共用 handler
24
pass:
li gp, 1
ebreak
trap_handler:
csrr t0, mcause
li t1, 3
bne t0, t1, unexpected_trap
la t2, result_code
sw gp, 0(t2)
la t3, done
csrw mepc, t3
mret
done:
fence
1: j 1b
mcause=3 表示正常出口。意外异常分支写入 0xdead。
result_code 保存结论，observed_vl 保存实际观察值。
文档代码节选；GitHub Issue #5766
Notes: 来源：XiangShan-V扩展issue与PoC提取.md
https://github.com/OpenXiangShan/XiangShan/issues/5766

## Slide 25
模板 2：gp 自校验与 tohost 退出
#5829，省略前置寄存器初始化与通用 handler
25
vsetivli x0, 2, e64, m1, ta, ma
vmv.v.i v9, 0
vsetivli x0, 1, e32, m1, tu, mu
la x10, data_word
vle32.v v9, (x10)
vmv.x.s x15, v9
li x16, 0xffffffffe01d7b92
li gp, 1
beq x15, x16, exit
li gp, 2
exit:
la t1, tohost
sd gp, 0(t1)
li t0, 0
.insn i 0x6b, 0, x0, t0, 0
gp 记录自校验结果，tohost 写出结论，GOODTRAP 收尾。
通用 handler 按 16/32 位指令长度跳过故障指令。
文档代码节选；GitHub Issue #5829
Notes: 来源：XiangShan-V扩展issue与PoC提取.md
https://github.com/OpenXiangShan/XiangShan/issues/5829

## Slide 26
模板 3：env-p 的权限与特权级构造
#6576，部分确认 / 分支相关条目
26
li t0, MSTATUS_VS
csrs mstatus, t0
li t0, -1
csrw pmpaddr0, t0
li t0, 0x1c
csrw pmpcfg0, t0
la s2, target
li t4, 4
li t0, MSTATUS_MPP
csrc mstatus, t0
la t0, umode
csrw mepc, t0
mret
umode:
vsetivli t0, 4, e32, m1, tu, mu
vlse32.v v3, (s2), t4
NAPOT 覆盖全地址空间，X-only 允许 U 模式取指。
经 mret 降权后 load 触发 access fault，观察 mtval。
文档代码节选；GitHub Issue #6576
Notes: 来源：XiangShan-V扩展issue与PoC提取.md
https://github.com/OpenXiangShan/XiangShan/issues/6576

## Slide 27
模板 4：生成器固定运行时
#5772，初始化、模式切换与跳过 handler 节选
27
trap_vec_init:
la x13, other_exp
csrw 0x305, x13
la x13, other_exp_s
csrw 0x105, x13
mepc_setup:
la x13, init
csrw 0x341, x13
# 省略 init_env 中的 mstatus、PMP、mie 初始化
mret
other_exp:
csrr x13, 0x341
addi x13, x13, 4
csrw 0x341, x13
mret
运行时预装 M/S 态 handler，并通过 mepc 与 mret 进入初始化段。
此 handler 固定将 mepc 增加 4。
文档代码节选；GitHub Issue #5772
Notes: 来源：XiangShan-V扩展issue与PoC提取.md
https://github.com/OpenXiangShan/XiangShan/issues/5772

## Slide 28
模板 4：寄存器初值与随机指令流
#5772，完整附件 vmv4r_illInstr.S 的结构节选
28
init:
fsrmi 2
li x0, 0xdb7d548a56e8beda
fmv.h.x f0, x0
li x1, 0x492bf97bfac3d9cc
fmv.w.x f1, x1
# 省略其余寄存器初始化
la t6, mem_region
j main
main:
li x27, 0x600
csrrs x0, mstatus, x27
vsetivli s3, 25, e8, m1, ta, ma
# 省略随机混合指令流
vmv4r.v v12, v22
固定骨架承载随机初值和指令流，目标指令夹在序列中。
文档记录 lhb-sec 系列还经过 seed.elf、差分报错与最小化。
文档代码节选；GitHub Issue #5772
Notes: 来源：XiangShan-V扩展issue与PoC提取.md
https://github.com/OpenXiangShan/XiangShan/issues/5772

## Slide 29
模板中的上下文构造机制（1）
29
机制 | 文档中的代码 / 状态 | 代表 Issue
前导指令自构造 | 两次 vsetivli、vmv 哨兵、li + sd | #5829 / #5840 / #5933
CSR 定向写 | vcsr、vstart、sstatus 精确赋值 | #6561
内存权限地图 | PMP deny、X-only、页表权限 | #5766 / #6576 / #6540
异常链与 handler | 第一次 fault 后恢复，再触发第二次 | #6399 / #6482 / #6540
Notes: 来源：XiangShan-V扩展issue与PoC提取.md，第三部分。

## Slide 30
模板中的上下文构造机制（2）
30
机制 | 文档中的代码 / 状态 | 代表 Issue
指令间时序邻近 | vsetvli 或 FOF 后立即 csrr vl | #5739 / #5766
数据与地址布局 | 符号位、NaN-box、未对齐、零 stride | #5829 / #5830 / #5933
微架构状态 | store 压力、队列回绕、提交进度 | #6467 / #6015
生成策略来源 | 符号求解、随机 fuzz、真实 workload | 文档机制 8
Notes: 来源：XiangShan-V扩展issue与PoC提取.md，第三部分。

## Slide 31
固定模板之外的材料与方式
31
方式 | 文档中的实例 | 材料特点
真实 workload | #2890，am-klib 程序 | 循环跨多次 vsetvli，自然形成上下文
静态 RTL 分析 | #5768 / #6168 | 引用译码条件或实现代码，无执行 PoC
维护者内部复现 | #5943 | 公开材料只有现象与指令
随机 fuzz 与最小化 | #6015 / #6482 / #6561 | 运行时固定，指令流与上下文随机
Notes: 来源：XiangShan-V扩展issue与PoC提取.md，第三部分。

## Slide 32
真实 workload：ASCII 转 UTF-16
#2890，历史混合问题 / 部分确认
32
1:
vsetvli t0, a2, e8, m1, ta, ma
vle8.v v0, (a1)
vsetvli x0, x0, e16, m2, ta, ma
vzext.vf2 v8, v0
vse16.v v8, (a0)
add a1, a1, t0
sub a2, a2, t0
slli t0, t0, 1
add a0, a0, t0
bnez a2, 1b
ret
循环读取字节、扩展为 16 位并写回，逐轮推进指针与剩余长度。
文档将其列为真实负载，包含 RTL 修复与环境配置的混合历史。
文档代码节选；GitHub Issue #2890
Notes: 来源：XiangShan-V扩展issue与PoC提取.md
https://github.com/OpenXiangShan/XiangShan/issues/2890

## Slide 33
文档归纳的验证方法
33
参考执行：Spike 或 NEMU 独立运行，得到参考行为。
差分执行：XiangShan --diff 运行同一 ELF，定位 PC、寄存器或 CSR 分歧。
独立复跑：XiangShan --no-diff，进一步区分 RTL、差分器与参考模型问题。
Notes: 来源：XiangShan-V扩展issue与PoC提取.md，方法模板：验证三件套。

## Slide 34
已确认 RTL 问题的代码分组（1）
按目标触发代码与观察点归组，共 28 条，含 1 条重复映射
34
代码形态 | Issue | 共同结构
配置 / CSR | #5739、#6561 | 配置或状态写入后立即观察 CSR
数据 / 标量扩展 | #5829、#5830、#5840、#5928 | 不同位宽、符号位、完整结果读回
mask / tail | #5765 | 先清寄存器，再 load / store mask
非法编码 / 上下文 | #5772、#5809、#5865 | 非法组对齐、vill、vd=v0
合法访存数据 | #5831、#5832、#5932、#5933、#5934 | mixed-EEW、whole、segment

## Slide 35
已确认 RTL 问题的代码分组（2）
按目标触发代码与观察点归组，共 28 条，含 1 条重复映射
35
代码形态 | Issue | 共同结构
FOF | #5766、#5767、#5930、#5931 | 受控 fault 或 active 数据比较
异常地址链 | #5943、#6399、#6482、#6540 | 故障地址与连续异常后状态
访存活性 | #6015、#6022 | 未映射地址和提交进度；含重复
流水队列 | #6467 | 压力前序、inactive store、回绕
静态实现 / 调试 | #5768、#6168 | 有实现代码，未提供完整执行 PoC

## Slide 36
PoC：配置后立即读取 vl
配置与 CSR 组，原帖 #5739 的最小程序
36
li t6, 0x600
csrs mstatus, t6
li a0, 16
vsetvli t1, a0, e8, m1, ta, ma
csrr t2, vl
预期 t1=t2=16，原始故障为 t2=0。
维护者定位 VL bypass 错误并给出修复 PR #5743。
原帖：github.com/OpenXiangShan/XiangShan/issues/5739
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5739。展示原始代码节选，不是独立可运行的完整测试。

## Slide 37
PoC：vl=0 时的 VS 状态副作用
配置与 CSR 组，原帖 #6561 的 failing seed
37
main:
csrwi vcsr, 4
csrwi vstart, 0
vsetivli zero, 0, e64, m1, tu, ma
fmv.x.d s7, fa0
csrrw t2, sstatus, s7
vsseg4e32.v v13, (t6), v0.t
初值 fa0=0xffffffffbf361d42，使 VS=Clean。
本例 vstart=0、vl=0，观察 VS 是否错误变 Dirty，不能忽略 vstart 条件。
原帖：github.com/OpenXiangShan/XiangShan/issues/6561
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/6561。展示原始代码节选，不是独立可运行的完整测试。

## Slide 38
PoC：窄整数移到标量后的符号扩展
数据扩展组，原帖 #5829 的 user_code 节选
38
vsetivli x0, 2, e64, m1, ta, ma
vmv.v.i v9, 0
vsetivli x0, 1, e32, m1, tu, mu
la x10, data_word
vle32.v v9, (x10)
vmv.x.s x15, v9
li x16, 0xffffffffe01d7b92
li gp, 1
beq x15, x16, exit
li gp, 2
data_word 的值为 0xe01d7b92，预期 x15 为其 XLEN 符号扩展。
省略 VS/FS 初始化、trap handler、退出和数据段，其余扩展类按完整目标结果比较。
原帖：github.com/OpenXiangShan/XiangShan/issues/5829
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5829。展示原始代码节选，不是独立可运行的完整测试。

## Slide 39
PoC：mask load 后完整读回
mask / tail 组，原帖 #5765 节选
39
li a0, 16
vsetvli t0, a0, e8, m1, tu, mu
vmv.v.i v0, 0
li a0, 10
vsetvli t0, a0, e8, m1, tu, mu
la a1, mask_data
vlm.v v0, (a1)
la a2, out_data
vsm.v v0, (a2)
mask_data 与 expected_data 均为 .byte 0x80, 0x03。
原程序逐字节比较读回数据，省略初始化、比较循环和 trap handler。
原帖：github.com/OpenXiangShan/XiangShan/issues/5765
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5765。展示原始代码节选，不是独立可运行的完整测试。

## Slide 40
PoC：非法 vtype 后执行向量指令
非法编码 / 上下文组，原帖 #5809 的关键序列
40
vsetvli x21, x21, 992
csrr x23, vl
csrr x22, vtype
vmv.x.s x21, v16
原日志：vl=0，vtype=0x8000000000000000（vill=1）。
预期 mcause=2、mtval=0x43002ad7。原故障却提交了 x21 写回。
原帖：github.com/OpenXiangShan/XiangShan/issues/5809
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5809。展示原始代码节选，不是独立可运行的完整测试。

## Slide 41
PoC：零 stride 的 segment load
合法访存数据组，原帖 #5933 的触发指令节选
41
li x9, 0x8fffffb8
li x10, 0x3803444b2551a2ae
sd x10, 16(x9)
li x10, 0x1000
sd x10, 24(x9)
# ... original intervening instructions omitted ...
li x8, 0x8fffffcd
vlsseg3e64.v v18, (x8), x19
原始触发状态：SEW=64、LMUL=1、x19=0，base 未对齐。
节选保留关键内存写入与目标指令，其余前置代码见原帖，逐 field 比较 active 数据。
原帖：github.com/OpenXiangShan/XiangShan/issues/5933
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5933。展示原始代码节选，不是独立可运行的完整测试。

## Slide 42
PoC：FOF 后立即读取缩短的 vl
FOF 组，原帖 #5766 的 payload 节选
42
li a0, 8
vsetvli t3, a0, e8, m1, tu, mu
vmv.v.i v8, 0
la a1, deny_start
addi a1, a1, -7
vle8ff.v v8, (a1)
csrr t4, vl
la t0, observed_vl
sw t4, 0(t0)
原程序用 PMP 将 deny_start 至 deny_end 设为不可访问。
前 7 字节可访问，第 8 字节 fault：期望读取 vl=7，原报告得到 0。
原帖：github.com/OpenXiangShan/XiangShan/issues/5766
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5766。展示原始代码节选，不是独立可运行的完整测试。

## Slide 43
PoC：FOF segment 的后元素 fault
FOF 组，原帖 #5767 的 payload 节选
43
li a0, 8
vsetvli t3, a0, e8, m1, tu, mu
vmv.v.i v16, 0
vmv.v.i v17, 0
la a2, deny_start
addi a2, a2, -12
vlseg2e8ff.v v16, (a2)
csrr t4, vl
同样使用 PMP deny 区，nf=2，每元素占 2 字节，故障落在后续元素。
原报告触发内部 critical error，期望按 FOF 语义处理。省略 PMP 初始化和 handler。
原帖：github.com/OpenXiangShan/XiangShan/issues/5767
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5767。展示原始代码节选，不是独立可运行的完整测试。

## Slide 44
PoC：向量异常后的标量异常
连续异常 / fault 地址组，原帖 #6399 的关键序列
44
vsetivli x0, 4, e32, m1, ta, ma
vsse32.v v11, (t4), s1
li a5, 0x0000020000000000
li t2, 0x917af882bf50788e
srl t6, t2, a5
sb sp, -1918(t6)
向量 store 与后续标量 store 依次触发 access fault。
原程序通过 handler 恢复执行，检查第二次 mtval 为本次地址，不能残留第一次地址。
原帖：github.com/OpenXiangShan/XiangShan/issues/6399
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/6399。展示原始代码节选，不是独立可运行的完整测试。

## Slide 45
PoC：未映射地址上的 indexed load 挂死
访存活性组，原帖 #6015 的反汇编摘录
45
80001234: fcvt.d.l fa7, a7
80001238: sha256sum0 s7, a7
8000123c: aes64ds sp, s6, s7
80001240: vluxei32.v v25, (a1), v17
80001244: aes64ks2 s4, s4, a4
a1=0x4ff0b1eb，VL=4，SEW=32，LMUL=1，各索引地址落入未映射区域。
观察异常与提交进度，原报告有 15000 周期无提交。附件提供 ELF，不是汇编源码。
原帖：github.com/OpenXiangShan/XiangShan/issues/6015
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/6015。展示原始代码节选，不是独立可运行的完整测试。

## Slide 46
流水队列 PoC：必须保留压力前序
46
#6467 原帖故障指令：vse16.v v10, (t1)，t1=0x80060050。
触发依赖：队列接近回绕、已提交 inactive 项、dataQueue 非空。单独一条 store 不能代表完整复现程序。
原始观察：deqPtr 超过 rdataPtr 的 assertion；禁用 assertion 后出现 store commit 地址 / mask 差异。
维护者确认 deqPtr 更新问题，并说明非对称门控本身是设计选择。附件列出源码与反汇编，此次下载未成功。
Notes: https://github.com/OpenXiangShan/XiangShan/issues/6467
[{"url": "https://github.com/OpenXiangShan/XiangShan/issues/6467#issuecomment-5506320043", "body": "Thanks for your report. We'll look into this.", "user": {"login": "ChrisYzcc", "name": "ChrisYzcc", "email": null, "avatar_url": "https://avatars.githubusercontent.com/u/117955876?v=4", "id": 117955876}, "id": 5506320043, "pull_request_review_id": null, "in_reply_to_id": null, "created_at": null, "updated_at": null, "review": null, "side": null, "line": null, "start_line": null, "path": null, "body_html": "<p dir=\"auto\">Thanks for your report. We'll look into this.</p>"}, {"url": "https://github.com/OpenXiangShan/XiangShan/issues/6467#issuecomment-5522852062", "body": "Thank you for your report! About your question:\n\n1. That's indeed a bug of `deqPtr` update, and it's the first time to be observed.\n2. The asymmetric `dataQueue.io.empty` gate between the `deqPtr` (:1272) and `rdataPtr` (:1302) inactive skips is intentional. We fixed it in #6474\n3. The vector unit of tip is under refactor, it may **can't execute complex vector instruction** (such as **stride** or **index** vector memory instruction) . The bug report base on `68901834` is all right.\n4. You can construct a test case: use a large number of stores with different cache lines to cause `Sbuffer` to have **L1 miss evictions** and then perform inactive vector stores.", "user": {"login": "weidingliu", "name": "weidingliu", "email": null, "avatar_url": "https://avatars.githubusercontent.com/u/47169884?v=4", "id": 47169884}, "id": 5522852062, "pull_request_review_id": null, "in_reply_to_id": null, "created_at": null, "updated_at": null, "review": null, "side": null, "line": null, "start_line": null, "path": null, "body_html": "<p dir=\"auto\">Thank you for your report! About your question:</p>\n<ol dir=\"auto\">\n<li>That's indeed a bug of <code class=\"notranslate\">deqPtr</code> update, and it's the first time to be observed.</li>\n<li>The asymmetric <code class=\"notranslate\">dataQueue.io.empty</code> gate between the <code class=\"notranslate\">deqPtr</code> (:1272) and <code class=\"notranslate\">rdataPtr</code> (:1302) inactive skips is intentional. We fixed it in <a class=\"issue-link js-issue-link\" data-error-text=\"Failed to load title\" data-id=\"5334191581\" data-permission-text=\"Title is private\" data-url=\"https://github.com/OpenXiangShan/XiangShan/issues/6474\" data-hovercard-type=\"pull_request\" data-hovercard-url=\"/OpenXiangShan/XiangShan/pull/6474/hovercard\" href=\"https://github.com/OpenXiangShan/XiangShan/pull/6474\">#6474</a></li>\n<li>The vector unit of tip is under refactor, it may <strong>can't execute complex vector instruction</strong> (such as <strong>stride</strong> or <strong>index</strong> vector memory instruction) . The bug report base on <code class=\"notranslate\">68901834</code> is all right.</li>\n<li>You can construct a test case: use a large number of stores with different cache lines to cause <code class=\"notranslate\">Sbuffer</code> to have <strong>L1 miss evictions</strong> and then perform inactive vector stores.</li>\n</ol>"}]

## Slide 47
静态代码证据：FOF 的 watchpoint 丢失
#6168，维护者确认 known issue；原帖不是完成的汇编 PoC
47
when(!entry.fof || vstart === 0.U){
entry.vstart := vstart
entry.exceptionVec := selExceptionVec
entry.uop.trigger := selPort.trigger // trigger only saved here
entry.vaddr := vaddr
...
}.otherwise{
entry.vl := Mux(entry.vl < vstart, entry.vl, vstart) // trigger lost
}
后元素 FOF 进入 otherwise 分支，仅更新 vl，原报告指出 trigger 未保存。
#5768 同样以 frm 检查的实现条件为证据，二者需要另建执行级测试。
原帖：github.com/OpenXiangShan/XiangShan/issues/6168
Notes: https://github.com/OpenXiangShan/XiangShan/issues/6168

## Slide 48
性能代码单列：LMUL=2 的吞吐测试
#4190 原帖 bench_vaddvv_m2 节选，UNROLL=8，LOOP=64
48
vsetvli t0, x0, e32, m2, ta, ma
li a0, LOOP
csrr a1, cycle
1:
.rept UNROLL
vadd.vv v8,v16,v24
vadd.vv v10,v18,v26
vadd.vv v12,v20,v28
vadd.vv v14,v22,v30
.endr
addi a0, a0, -1
bnez a0, 1b
fence.i
csrr a0, cycle
sub a0, a0, a1
观察 cycle 差值。维护者确认不必要的 vd 依赖并给出 PR #4198，
LMUL=1 的每周期解码限制则是另一项设计取舍。
原帖：github.com/OpenXiangShan/XiangShan/issues/4190
Notes: https://github.com/OpenXiangShan/XiangShan/issues/4190

## Slide 49
PoC 可用性与解释边界
49
完整源码、关键指令节选、反汇编和实现代码分别标注，不能视作同一种证据。
#5772 附件包含 .S 源码；#6015 附件仅有 1 个 ELF；#6482 附件含 98 个 ELF。
#5768 / #6168 只有实现级证据或未完成执行 PoC；#6467 的压力程序附件本次未成功下载。
#2890 混合历史 RTL 修复、nexus-am 与配置问题；#6576 有 v2 修复线索和 v3 移植计划，均不整帖计入严格确认 RTL 数。

## Slide 50
Mutation 建议：围绕触发条件做变异
以下是基于真实 PoC 的测试设计建议，不是已完成的实验结果
50
先保留原始 PoC 的分支、commit、初值、内存布局与 oracle，建立能够稳定运行的基线。
每次改变一个关键维度，并加入相邻合法或无故障对照，再做有约束的组合覆盖。
保留预期非法和内存异常样本，不能只回放 Retire_Success。目标指令后增加 CSR、寄存器或内存观察。
每个变体关联原 Issue；输入不同不等于新的根因。性能、参考模型和 RTL 结果分别统计。

## Slide 51
Mutation：CSR、数据与合法性
51
目标形态 | 优先变异 | 必须保持与观察
配置 / CSR | AVL、SEW、LMUL；CSR 相邻距离 | 保持可执行配置，比较返回 rd 与新 vl
VS 状态副作用 | vl=0/1；vstart=0/非0；Clean/Dirty | 区分是否改变向量状态，再判断 Dirty
数据扩展 / NaN-box | SEW、符号边界、扩展倍率 | 完整标量 / 向量读回，高位必须检查
mask / tail | vl 边界、位图、tu/ta、mu/ma | 先写唯一哨兵，期望遵循具体策略
非法编码 / 上下文 | vill、组对齐、reserved 字段 | 修改字段时保留其他前提，检查 trap

## Slide 52
Mutation：内存、异常与活性
52
目标形态 | 优先变异 | Oracle / 对照
合法 load / store | stride=0/非0，nf、EEW、base 对齐 | 每 lane / field 唯一数据，完整读回
FOF | fault 位于首/后元素；PMP 边界 | vl、部分结果、异常种类，无故障对照
连续 fault | 地址 A/B、load/store 方向、特权级 | mtval/stval 应属于本次 fault
队列 / 活性 | cache-line 压力、inactive 项、回绕 | 提交进度、assertion、commit 地址
调试 / 性能 | watchpoint 与 FOF；依赖与 LMUL | 调试事件独立监测，性能单列 cycle

## Slide 53
建议实施顺序
53
第一阶段：使用已有真实源码，补齐 CSR、标量扩展、mask、非法指令的明确 oracle。
第二阶段：搭建可控内存与 trap handler，按 FOF、segment、连续 fault 的原始结构扩展。
第三阶段：保留压力序列与提交日志，覆盖队列回绕、挂死及调试触发器，性能使用独立预算。
每次输出记录关联 Issue、原始 PoC、变异参数和完整初值，附预期/实际结果及最小化程序。
确认问题与变体分别计数。