## Slide 1
XiangShan V 扩展 Issue
1
统计、确认依据与真实 PoC
代码分类与 Mutation 建议
固定集合：89 个 Issue 核查日期：2026-09-17
Notes: 来源：isla工作区原始89条Issue清单，以及对应GitHub原帖、标签和评论。

## Slide 2
Issue 集合概况
原始清单固定为 89 个 Issue，元数据按 GitHub 原帖校准
2
统计项 | 结果
Issue 总数 | 89
作者数 | 22
创建时间范围（UTC） | 2024-04-16 至 2026-09-16
当前 Open / Closed | 57 / 32
范围说明 | 包含 RTL、工具、重复、讨论与性能条目

## Slide 3
作者数量与发帖时间（1）
时间为该作者在本次 89 条集合中的最早和最晚创建日期（UTC）
3
作者 | Issue | Open | Closed | 创建日期范围
lhb-sec | 20 | 19 | 1 | 2026-05-25 至 2026-09-11
KnightGOKU | 14 | 10 | 4 | 2026-03-25 至 2026-05-10
wndmll643 | 8 | 6 | 2 | 2026-07-21 至 2026-09-16
youzi27 | 8 | 5 | 3 | 2025-11-29 至 2026-05-11
jimmymtest | 6 | 6 | 0 | 2026-04-20 至 2026-04-22
LeeHaofeng | 5 | 3 | 2 | 2026-06-07 至 2026-06-13
zhangkanqi | 5 | 3 | 2 | 2026-04-06 至 2026-04-08
camel-cdr | 4 | 0 | 4 | 2024-04-16 至 2025-01-16
cesarus777 | 3 | 0 | 3 | 2025-12-24 至 2025-12-24
nyh1 | 3 | 0 | 3 | 2026-05-28 至 2026-05-28
maplejty814 | 2 | 2 | 0 | 2026-06-26 至 2026-06-29

## Slide 4
作者数量与发帖时间（2）
时间为该作者在本次 89 条集合中的最早和最晚创建日期（UTC）
4
作者 | Issue | Open | Closed | 创建日期范围
0x1B05 | 1 | 1 | 0 | 2026-05-14 至 2026-05-14
biquanha | 1 | 0 | 1 | 2026-03-19 至 2026-03-19
cyyself | 1 | 0 | 1 | 2024-05-27 至 2024-05-27
H-Y-B | 1 | 0 | 1 | 2024-11-29 至 2024-11-29
Hoshi44 | 1 | 1 | 0 | 2026-04-05 至 2026-04-05
I3eg1nner | 1 | 0 | 1 | 2025-12-26 至 2025-12-26
jlong299 | 1 | 0 | 1 | 2024-12-10 至 2024-12-10
kds1123001 | 1 | 0 | 1 | 2026-08-24 至 2026-08-24
msuadOf | 1 | 0 | 1 | 2026-08-24 至 2026-08-24
Security-HC | 1 | 1 | 0 | 2026-06-26 至 2026-06-26
WaltJr-OH | 1 | 0 | 1 | 2025-03-06 至 2025-03-06

## Slide 5
Issue 创建时间分布
2026 年 75 条，2025 年 8 条，2024 年 6 条
5
Chart: 
| 03月 | 04月 | 05月 | 06月 | 07月 | 08月 | 09月
Issue数量 | 3 | 18 | 21 | 10 | 8 | 3 | 12
图中仅展示本次集合的 2026 年分布，不代表全仓库缺陷发生率。

## Slide 6
香山确认的判定口径
标签、最终评论、问题归属与修复证据分别记录
6
确认依据：明确的 confirmed / fixed 标签，或维护者对该问题的确认、修复说明。
归属另行判断：已确认问题可能属于 RTL、DiffTest、NEMU 或性能，不能合并统计。
Open / Closed 与修复分开：#6561、#6015 仍 Open，但评论已有修复记录。
WIP、reported 或“稍后检查”不构成确认。分支线索与混合历史问题单列。
Notes: 逐条证据见服务器 V扩展issue核验与PoC数据.json。

## Slide 7
89 条 Issue 的核验结果
7
归类 | 数量 | 说明
已确认 RTL / 调试 | 28 | 含 1 条重复映射 #6022
已确认工具问题 | 2 | #5279 DiffTest，#5426 NEMU
已确认性能问题 | 1 | #4190 的不必要依赖
行为对齐记录 | 1 | #5725，维护者说明非功能 Bug
部分确认 / 分支相关 | 2 | #2890、#6576，不能整帖直接计数
无效 / 非功能 / 重复等 | 27 | 含维护者否认、报告者撤回、历史记录
尚无充分确认依据 | 28 | 保留为待核查报告
合计 | 89 | 按 Issue 计数，不等于独立 Bug 数

## Slide 8
确认结论中的关键区别
8
#6467：reported / WIP 标签仍在，但维护者明确确认 deqPtr 更新 Bug，并指向 PR #6474。
#6168：维护者明确称为 known issue，属于调试触发器问题；原帖还没有完成可执行 PoC。
#5279 / #5426：分别属于 DiffTest 与 NEMU。#5725 属于保留行为的实现对齐。
#6039：现有 9 个本地 PoC 的关联 Issue，目前仍是待确认报告，不列入后面的已确认 RTL 主表。
Notes: 具体评论链接在89条明细页的备注与远程报告中。

## Slide 9
全量 Issue 清单（1/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
9
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6576 | 2026-09-16 | wndmll643 | Open | 部分确认 | vlse32.v 异常 mtval
#6561 | 2026-09-11 | lhb-sec | Open | 确认/修复 | vl=0 / VS Dirty
#6555 | 2026-09-11 | wndmll643 | Closed | 报告撤回 | vssubu.vx / vxsat
#6545 | 2026-09-10 | lhb-sec | Open | 待确认 | masked vsrl.vv 挂死
#6544 | 2026-09-10 | lhb-sec | Open | 待确认 | vcpop.m 非对齐组
#6543 | 2026-09-10 | lhb-sec | Open | 待确认 | vdiv.vx 除零挂死
#6540 | 2026-09-10 | wndmll643 | Open | 确认RTL | 向量/标量页错 stval
Notes: #6576 `mtval` is not written on a load access fault taken by a vector strided load (`vlse32.v`) — kunminghu-v3
https://github.com/OpenXiangShan/XiangShan/issues/6576
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6576", "label_snapshot": "module: memory, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6576#issuecomment-5692218398", "summary": "维护者认为v2由PR6548修复，v3计划移植；分支相关线索单列，不视为当前v3已完整确认/修复", "quote": "I think this issue has been fixed in `kunminghu-v2`. See PR https://github.com/OpenXiangShan/XiangShan/pull/6548.\nVector support for `kunminghu-v3` is still under development, and we'll apply the corresponding fixes to v3 in the future.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6561 Incorrect `mstatus.VS` Dirty update for `vl=0` vector memory instructions
https://github.com/OpenXiangShan/XiangShan/issues/6561
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6561", "label_snapshot": "type: bug/confirmed, module: backend, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6561#issuecomment-5661448507", "summary": "confirmed 标签；维护者说明已在 PR #6570 修复，报告者回测通过。", "quote": "If the value of the `vstart` register is 0, a `vector store` instruction will not alter the vector state and therefore will not generate a `DirtyVS`; if the value of the `vstart` register is not 0, all successfully executed vector instructions will reset `vstart` to `0` upon completion, thereby altering the vector state and generating a `DirtyVS`.\nI have fixed this in this PR. [https://github.com/OpenXiangShan/XiangShan/pull/6570](https://github.com/OpenXiangShan/XiangShan/pull/6570)\nI successfully ran the test cases locally.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6555 `vssubu.vx` (vector fixed-point unsigned saturating subtract) does not set `vxsat` when it saturates — kunminghu-v3
https://github.com/OpenXiangShan/XiangShan/issues/6555
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6555", "label_snapshot": "module: backend, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6555#issuecomment-5642683809", "summary": "报告者：implementation-defined behavior, not a bug，关闭Issue", "quote": "Thanks for your reply. While re-analyzing some other bug, I found out that this is an implementation-defined behavior, not a bug. Closing the issue.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6545 `vsrl.vv` with `v0.t` mask hangs and never writes back the destination register
https://github.com/OpenXiangShan/XiangShan/issues/6545
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6545", "label_snapshot": "module: backend, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6545", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6544 `vcpop.m` is incorrectly reported as an illegal instruction when `LMUL=8` and `vs2` is not group-aligned
https://github.com/OpenXiangShan/XiangShan/issues/6544
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6544", "label_snapshot": "module: backend, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6544", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6543 `vdiv.vx` with a zero divisor deadlocks the core
https://github.com/OpenXiangShan/XiangShan/issues/6543
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6543", "label_snapshot": "module: backend, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6543", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6540 `stval` mismatch on a scalar store **page** fault after a vector store **page** fault (S-mode) — kunminghu-v2
https://github.com/OpenXiangShan/XiangShan/issues/6540
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6540", "label_snapshot": "type: bug/confirmed, module: memory, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6540", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]

## Slide 10
全量 Issue 清单（2/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
10
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6536 | 2026-09-09 | lhb-sec | Open | 待确认 | vmadc.vi mask tail
#6486 | 2026-09-04 | wndmll643 | Open | 待确认 | vsseg2e16.v 数据
#6482 | 2026-09-04 | lhb-sec | Open | 确认RTL | 连续异常 mtval 陈旧
#6475 | 2026-09-03 | wndmll643 | Open | 待确认 | vsseg3e32.v uop 数
#6467 | 2026-09-02 | wndmll643 | Closed | 确认/修复 | StoreQueue 指针回绕
#6410 | 2026-08-24 | msuadOf | Closed | 无效报告 | move / merge 组对齐
#6407 | 2026-08-24 | kds1123001 | Closed | 无效报告 | 无效 VSEW 的 load
Notes: #6536 `vmadc.vi` zeroes mask-destination tail bits
https://github.com/OpenXiangShan/XiangShan/issues/6536
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6536", "label_snapshot": "module: backend, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6536", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6486 Legal segmented store `vsseg2e16.v` silently commits wrong store data (0 instead of the source value) — vector store-data unit emits 0 for a field on kunminghu-v3
https://github.com/OpenXiangShan/XiangShan/issues/6486
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6486", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6486", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6482 Stale mtval after consecutive same-direction RVV memory access faults
https://github.com/OpenXiangShan/XiangShan/issues/6482
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6482", "label_snapshot": "type: bug/confirmed, module: unknown, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6482", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#6475 Legal segmented store `vsseg3e32.v` triggers `robEntries uopNum is overflow!` (ROB uop-count underflow) — deterministic assertion abort on kunminghu-v3
https://github.com/OpenXiangShan/XiangShan/issues/6475
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6475", "label_snapshot": "type: bug/reported, module: backend, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6475", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6467 StoreQueue `deqPtr > rdataPtr` assertion fails at the physical-queue wrap boundary under vector stores
https://github.com/OpenXiangShan/XiangShan/issues/6467
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6467", "label_snapshot": "type: bug/reported, module: memory, module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6467#issuecomment-5522852062", "summary": "weidingliu：indeed a bug of deqPtr update；We fixed it in #6474", "quote": "1. That's indeed a bug of `deqPtr` update, and it's the first time to be observed.\n2. The asymmetric `dataQueue.io.empty` gate between the `deqPtr` (:1272) and `rdataPtr` (:1302) inactive skips is intentional. We fixed it in #6474", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6410 vmove-class instructions (vmv.v.*, vmerge.*) with misaligned register groups don't raise illegal instruction (test-matrix confirmed, extends #5772)
https://github.com/OpenXiangShan/XiangShan/issues/6410
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6410", "label_snapshot": "type: bug/invalid, module: backend, module: vector, type: bug/WIP feature"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6410", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6407 Vector load doesn't trigger illegal instruction trap when VSEW is invalid
https://github.com/OpenXiangShan/XiangShan/issues/6407
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6407", "label_snapshot": "type: bug/invalid, module: vector, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6407", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]

## Slide 11
全量 Issue 清单（3/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
11
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6399 | 2026-08-21 | lhb-sec | Open | 确认RTL | 连续 store fault mtval
#6302 | 2026-07-28 | lhb-sec | Open | 待确认 | reserved VSEW
#6298 | 2026-07-28 | lhb-sec | Open | 未实现 | vstart / 未实现指令
#6296 | 2026-07-28 | lhb-sec | Open | 待确认 | store fault mcause
#6295 | 2026-07-28 | lhb-sec | Open | 待确认 | FOF 目的寄存器
#6293 | 2026-07-28 | lhb-sec | Open | 待确认 | FOF / I/O PMA
#6292 | 2026-07-28 | wndmll643 | Open | 待确认 | 页错后的 vstart
Notes: #6399 `mtval` mismatch on scalar store access fault after a vector store access fault
https://github.com/OpenXiangShan/XiangShan/issues/6399
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6399", "label_snapshot": "type: bug/confirmed, module: backend, module: memory, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6399", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#6302 XiangShan does not trap on vector instruction with reserved vsew encoding
https://github.com/OpenXiangShan/XiangShan/issues/6302
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6302", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6302", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6298 XiangShan misses illegal-instruction trap for out-of-range vstart
https://github.com/OpenXiangShan/XiangShan/issues/6298
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6298", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6298#issuecomment-5542251829", "summary": "维护者明确unimplemented feature, not a bug", "quote": "I must claim that this issue just report a unimplemented feature, not a bug.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6296 Vector store reports wrong `mcause` in M-mode
https://github.com/OpenXiangShan/XiangShan/issues/6296
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6296", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6296", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6295 `vle32ff.v` corrupts destination vector register on Load Access Fault
https://github.com/OpenXiangShan/XiangShan/issues/6295
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6295", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6295", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6293 `vle64ff.v` misses Load Access Fault on misaligned access to I/O PMA region
https://github.com/OpenXiangShan/XiangShan/issues/6293
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6293", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6293", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6292 vstart set to wrong element on a page-faulting vector load (for debugging assistance)
https://github.com/OpenXiangShan/XiangShan/issues/6292
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6292", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6292", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]

## Slide 12
全量 Issue 清单（4/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
12
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6289 | 2026-07-27 | lhb-sec | Open | 待确认 | fault 后 AMO 活性
#6262 | 2026-07-21 | wndmll643 | Open | 待确认 | 未映射页 segment
#6168 | 2026-06-29 | maplejty814 | Open | 确认RTL | FOF watchpoint 丢失
#6152 | 2026-06-26 | Security-HC | Open | 待确认 | 扩展结果高位
#6151 | 2026-06-26 | maplejty814 | Open | 无效报告 | vl=0 segment 性能
#6093 | 2026-06-13 | LeeHaofeng | Closed | 无效报告 | 浮点冗余舍入代码
#6085 | 2026-06-11 | lhb-sec | Open | 待确认 | indexed store 提交
Notes: #6289 AMO deadlocks after `vse32.v` store access fault
https://github.com/OpenXiangShan/XiangShan/issues/6289
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6289", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6289", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6262 XS bug-report — vlseg to unmapped page deadlocks (VSegmentUnit)
https://github.com/OpenXiangShan/XiangShan/issues/6262
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6262", "label_snapshot": "module: vector, type: bug/WIP feature"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6262", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6168 [Bug] debug watchpoint trigger lost on FOF non-first element
https://github.com/OpenXiangShan/XiangShan/issues/6168
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6168", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6168#issuecomment-4913753242", "summary": "维护者确认known issue，计划后续修复", "quote": "This is a known issue. We are evaluating the specific matters for subsequent fixes. Thank you for your point.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6152 [RVV] vzext.vf4 / vsext.vf4 writes zero to high 64-bit (elements 2..3)
https://github.com/OpenXiangShan/XiangShan/issues/6152
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6152", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6152", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6151 [Performance] VSegmentUnit: segment instructions with vl=0 stall the memory unit hundreds of cycles instead of retiring immediately
https://github.com/OpenXiangShan/XiangShan/issues/6151
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6151", "label_snapshot": "type: bug/invalid, topic: performance, module: vector, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6151", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6093 ```VectorFloatAdder.scala``` overflow rounding uses wrong normal-path GRS bits
https://github.com/OpenXiangShan/XiangShan/issues/6093
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6093", "label_snapshot": "type: bug/invalid, module: vector"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6093", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6085 `vsoxei32.v` fails to commit store
https://github.com/OpenXiangShan/XiangShan/issues/6085
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6085", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6085", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]

## Slide 13
全量 Issue 清单（5/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
13
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6079 | 2026-06-10 | lhb-sec | Open | 待确认 | whole load 的 vstart
#6066 | 2026-06-07 | LeeHaofeng | Closed | 无效报告 | 废弃 VMask 模块
#6065 | 2026-06-07 | LeeHaofeng | Open | 待确认 | genVUopOffset 的 nf
#6064 | 2026-06-07 | LeeHaofeng | Open | 待确认 | VPermSrcType 条件
#6063 | 2026-06-07 | LeeHaofeng | Open | 明确非Bug | vfrec7 / fflags 格式
#6042 | 2026-05-29 | lhb-sec | Open | 待确认 | load fault 的 vstart
#6039 | 2026-05-28 | lhb-sec | Open | 待确认 | rd=x0 的 vsetvl 活性
Notes: #6079 `vl1re16.v` incorrectly computes `vstart` on Load Access Fault
https://github.com/OpenXiangShan/XiangShan/issues/6079
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6079", "label_snapshot": "module: vector, type: bug/WIP feature"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6079", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6066 VMask.scala ```shift``` truncation bug for ```SEW=8``` and large ```uopIdx```
https://github.com/OpenXiangShan/XiangShan/issues/6066
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6066", "label_snapshot": "type: bug/invalid, module: vector, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6066", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6065 ```genVUopOffset``` uses wrong ```nf``` semantics
https://github.com/OpenXiangShan/XiangShan/issues/6065
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6065", "label_snapshot": "type: bug/reported, module: vector, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6065", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6064 Copy-Paste Typo in Mux1H Default Condition — ```isvrgatherei16``` Repeated Instead of ```isvcompress``` in VPermSrcTypeModule
https://github.com/OpenXiangShan/XiangShan/issues/6064
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6064", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6064", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6063 ```CVT16.scala``` fflags ```NV``` lost for ```vfrec7 -inf```
https://github.com/OpenXiangShan/XiangShan/issues/6063
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6063", "label_snapshot": "type: bug/reported, module: vector, version: kunminghu-v3"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6063#issuecomment-4678966210", "summary": "维护者说明fflags截断结果正确，仅代码格式问题，非功能bug", "quote": "Here `fflags0` is `5` bits, and the result after `Cat` is truncated to exactly `0`, so although it looks wrong, the result is correct.\nWe will fix the formatting issue in the `kunminghu-v3` branch later.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6042 `vle16.v` fault handling incorrectly sets `vstart` to `vl` instead of the faulting element index
https://github.com/OpenXiangShan/XiangShan/issues/6042
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6042", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6042", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6039 `vsetvl` with `rd=zero` causes core hang
https://github.com/OpenXiangShan/XiangShan/issues/6039
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6039", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6039", "summary": "只有 reported；维护者回复尚未 review/fix，不能视作确认。"}]

## Slide 14
全量 Issue 清单（6/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
14
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#6037 | 2026-05-28 | nyh1 | Closed | 无效报告 | vmvnr 寄存器对齐
#6036 | 2026-05-28 | nyh1 | Closed | 无效报告 | vmv1r / vstart
#6035 | 2026-05-28 | lhb-sec | Open | 待确认 | FOF 异常 CSR
#6034 | 2026-05-28 | nyh1 | Closed | 明确非Bug | vfsgnj / FS Dirty
#6022 | 2026-05-25 | lhb-sec | Closed | 确认/重复 | 向量 load 挂死重复
#6015 | 2026-05-25 | lhb-sec | Open | 确认/修复 | indexed load 未映射
#5958 | 2026-05-14 | 0x1B05 | Open | 待确认 | 跨页 / replay assertion
Notes: #6037 [Bug] vmvnr_unaligned_regs
https://github.com/OpenXiangShan/XiangShan/issues/6037
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6037", "label_snapshot": "type: bug/invalid, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6037", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6036 [Bug] vmv1r_vstart_ge_evl
https://github.com/OpenXiangShan/XiangShan/issues/6036
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6036", "label_snapshot": "type: bug/invalid, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6036", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#6035 `vle32ff.v` fails to update exception CSRs upon Load Access Fault
https://github.com/OpenXiangShan/XiangShan/issues/6035
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6035", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6035", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#6034 【BUG】 `vfsgnj.vv` incorrectly dirties `mstatus.FS`
https://github.com/OpenXiangShan/XiangShan/issues/6034
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6034", "label_snapshot": "type: bug/reported, module: backend"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6034#issuecomment-4570036662", "summary": "sinceforYy：We do not believe this is a bug；fflags功能正确", "quote": "We do not believe this is a bug.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6022 `vlse64.v` fails to trigger Load Access Fault upon illegal address access
https://github.com/OpenXiangShan/XiangShan/issues/6022
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6022", "label_snapshot": "type: bug/confirmed, note: duplicate, module: memory"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6022#issuecomment-4539692989", "summary": "confirmed 标签；维护者称已由 PR #6020 修复的 vec-load hang，作为 #6015 同根因映射，不独计根因。", "quote": "This is a known issue caused by a vec load hang; we have already fixed it.https://github.com/OpenXiangShan/XiangShan/pull/6020", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#6015 Pipeline hangs on `vluxei32.v` when accessing unmapped physical addresses
https://github.com/OpenXiangShan/XiangShan/issues/6015
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6015", "label_snapshot": "type: bug/confirmed, module: memory"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/6015#issuecomment-4539489076", "summary": "维护者可复现并称 \"indeed a bug\"，后称已由 PR #6020 修复。", "quote": "Thank you for your report! That's indeed a bug caused by `d38fc34`, we will fix it later!", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5958 Kunminghu-v2: LoadQueueReplay assertion on translated cross-page vector byte load/store
https://github.com/OpenXiangShan/XiangShan/issues/5958
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5958", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5958", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]

## Slide 15
全量 Issue 清单（7/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
15
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5943 | 2026-05-11 | youzi27 | Open | 确认RTL | vsse16.v 的 mtval
#5934 | 2026-05-10 | KnightGOKU | Open | 确认RTL | masked segment 数据
#5933 | 2026-05-10 | KnightGOKU | Open | 确认RTL | zero-stride segment
#5932 | 2026-05-10 | KnightGOKU | Open | 确认RTL | indexed segment 数据
#5931 | 2026-05-10 | KnightGOKU | Open | 确认RTL | misaligned FOF field
#5930 | 2026-05-10 | KnightGOKU | Open | 确认RTL | FOF active byte
#5929 | 2026-05-10 | KnightGOKU | Closed | 无效报告 | 参考模型内存大小
Notes: #5943 Incorrect `mtval` for faulting `vsse16.v` on kunminghu-v2
https://github.com/OpenXiangShan/XiangShan/issues/5943
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5943", "label_snapshot": "type: bug/confirmed, module: unknown, version: kunminghu-v2"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5943#issuecomment-4437990329", "summary": "confirmed 标签；维护者最终复现并明确 \"I think this issue is a bug\"。", "quote": "@youzi27 Ah ha, I finally reproduce this issue, I think this issue is a bug, which was introduced by (https://github.com/OpenXiangShan/XiangShan/commit/2bec9bddf90fa1ddd2690f344ef3f34e4346bb9e#diff-6db620258edc695befb5c4de9a76e239e89ff74d881e35a4ab978f931efb21aeR119) .", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5934 `vlseg2e16.v` corrupts an active destination lane during masked segment load
https://github.com/OpenXiangShan/XiangShan/issues/5934
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5934", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5934", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5933 `vlsseg3e64.v` loads wrong active destination data for zero-stride segment load
https://github.com/OpenXiangShan/XiangShan/issues/5933
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5933", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5933", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5932 `vluxseg5ei32.v` corrupts active destination data for indexed segment load
https://github.com/OpenXiangShan/XiangShan/issues/5932
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5932", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5932", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5931 `vlseg2e32ff.v` loads wrong field0 data for misaligned fault-only-first segment load
https://github.com/OpenXiangShan/XiangShan/issues/5931
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5931", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5931", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5930 `vle8ff.v` corrupts active loaded byte value
https://github.com/OpenXiangShan/XiangShan/issues/5930
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5930", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5930", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5929 `vloxseg5ei64.v` misses load access fault and commits destination vector registers
https://github.com/OpenXiangShan/XiangShan/issues/5929
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5929", "label_snapshot": "type: bug/invalid"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5929", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]

## Slide 16
全量 Issue 清单（8/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
16
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5928 | 2026-05-09 | youzi27 | Open | 确认RTL | vsext 元素选取
#5927 | 2026-05-09 | youzi27 | Closed | 自报重复 | vmv.x.s 重复报告
#5922 | 2026-05-09 | youzi27 | Closed | 自报重复 | frm 重复报告
#5921 | 2026-05-09 | youzi27 | Open | 待确认 | indexed store vstart
#5919 | 2026-05-08 | youzi27 | Open | 待确认 | reserved vmv<nr>r
#5865 | 2026-04-27 | KnightGOKU | Open | 确认RTL | vmerge 的 vd=v0
#5845 | 2026-04-22 | jimmymtest | Open | 待确认 | 三指令流水 assertion
Notes: #5928 Incorrect source element selection in `vsext`
https://github.com/OpenXiangShan/XiangShan/issues/5928
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5928", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5928", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5927 Incorrect scalar result from `vmv.x.s` when SEW is smaller than XLEN
https://github.com/OpenXiangShan/XiangShan/issues/5927
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5927", "label_snapshot": "note: duplicate"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5927#issuecomment-4412737115", "summary": "youzi27：This issue seems similar to #5829", "quote": "This issue seems similar to #5829 , so I will close it. Sorry for the confusion.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5922 Incorrect handling of invalid `frm` for `vfmerge.vfm`
https://github.com/OpenXiangShan/XiangShan/issues/5922
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5922", "label_snapshot": "note: duplicate"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5922#issuecomment-4411727439", "summary": "youzi27：This issue seems similar to #5768", "quote": "This issue seems similar to #5768 , so I will close it. Sorry for the confusion.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5921 Incorrect `vstart` update after faulting vector indexed store
https://github.com/OpenXiangShan/XiangShan/issues/5921
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5921", "label_snapshot": "module: memory, module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5921", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#5919 Reserved `vmv<nr>r.v` encodings are executed instead of being rejected
https://github.com/OpenXiangShan/XiangShan/issues/5919
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5919", "label_snapshot": "module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5919", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#5865 XiangShan misses illegal-instruction trap for reserved masked `vmerge.vvm` with vd = v0
https://github.com/OpenXiangShan/XiangShan/issues/5865
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5865", "label_snapshot": "type: bug/confirmed, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5865", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5845 [Assertion Failure] XiangShan crashes in `LoadUnitS0` on a reduced `vmsbf.m -> vl1re64.v -> vlseg4e8.v` sequence
https://github.com/OpenXiangShan/XiangShan/issues/5845
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5845", "label_snapshot": "type: bug/reported, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5845", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]

## Slide 17
全量 Issue 清单（9/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
17
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5840 | 2026-04-22 | jimmymtest | Open | 确认RTL | vzext.vf8 零扩展
#5832 | 2026-04-20 | jimmymtest | Open | 确认RTL | whole load 高位截断
#5831 | 2026-04-20 | jimmymtest | Open | 确认RTL | mixed-EEW strided
#5830 | 2026-04-20 | jimmymtest | Open | 确认RTL | vfmv.f.s NaN-box
#5829 | 2026-04-20 | jimmymtest | Open | 确认RTL | vmv.x.s 符号扩展
#5809 | 2026-04-14 | KnightGOKU | Closed | 确认/修复 | vill 后 vmv.x.s
#5808 | 2026-04-14 | KnightGOKU | Open | 待确认 | vsse16.v 的 vstart
Notes: #5840 [BUG] `vzext.vf8` can compute the wrong zero-extended result for an active destination element.
https://github.com/OpenXiangShan/XiangShan/issues/5840
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5840", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5840", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5832 [BUG] `vl8re64.v` truncates upper 64-bit data in whole-register loads
https://github.com/OpenXiangShan/XiangShan/issues/5832
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5832", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5832", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5831 [BUG] `vlse32.v` corrupts packed 32-bit element data under SEW=64, LMUL=8 mixed-EEW execution
https://github.com/OpenXiangShan/XiangShan/issues/5831
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5831", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5831", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5830 [BUG] `vfmv.f.s` fails to NaN-box 32-bit values when writing to a 64-bit floating-point registe
https://github.com/OpenXiangShan/XiangShan/issues/5830
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5830", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5830", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5829 [Bug] vmv.x.s instruction fails to sign-extend when SEW < XLEN
https://github.com/OpenXiangShan/XiangShan/issues/5829
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5829", "label_snapshot": "type: bug/confirmed, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5829", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5809 `vmv.x.s` executes instead of raising illegal-instruction when `vsetvli` leaves `vtype.vill=1`
https://github.com/OpenXiangShan/XiangShan/issues/5809
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5809", "label_snapshot": "module: backend, type: bug/fixed"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5809", "summary": "GitHub `type: bug/fixed` 标签；无 tool 标签，按 XiangShan 已确认且已有修复标签记录。"}]
#5808 `vstart` mismatch after a minimal `vsse16.v` RVV testcase
https://github.com/OpenXiangShan/XiangShan/issues/5808
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5808", "label_snapshot": "module: vector, type: bug/WIP feature"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5808", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]

## Slide 18
全量 Issue 清单（10/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
18
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5790 | 2026-04-08 | zhangkanqi | Closed | 无效报告 | 模型配置/自修改
#5777 | 2026-04-07 | zhangkanqi | Closed | 无效报告 | MinimalConfig 活性
#5772 | 2026-04-06 | zhangkanqi | Open | 确认RTL | vmv4r.v 组对齐
#5770 | 2026-04-06 | zhangkanqi | Open | 待确认 | 异常时部分写回
#5769 | 2026-04-06 | zhangkanqi | Open | 待确认 | indexed store mtval
#5768 | 2026-04-05 | Hoshi44 | Open | 确认RTL | FP move / merge frm
#5767 | 2026-04-05 | KnightGOKU | Open | 确认RTL | segment FOF 内部异常
Notes: #5790 Mismatch mcause and mtval when executing vssseg3e16.v
https://github.com/OpenXiangShan/XiangShan/issues/5790
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5790", "label_snapshot": "type: bug/invalid"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5790", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5777 No instructions have been submitted for a long time. Could this be a case of deadlock?
https://github.com/OpenXiangShan/XiangShan/issues/5777
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5777", "label_snapshot": "type: bug/invalid"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5777", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5772 vmv4r.v with misaligned registers dosen't raise illegal instruction exception
https://github.com/OpenXiangShan/XiangShan/issues/5772
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5772", "label_snapshot": "type: bug/confirmed, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5772", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5770 Vector whole register load(vl2re32.v) partially updates destination on exception
https://github.com/OpenXiangShan/XiangShan/issues/5770
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5770", "label_snapshot": "module: backend, module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5770", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#5769 Vector indexed segment store (vsuxseg*ei*) reports only base address in mtval on exception
https://github.com/OpenXiangShan/XiangShan/issues/5769
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5769", "label_snapshot": "module: backend, module: vector, type: bug/WIP feature, version: kunminghu-v3"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5769", "summary": "无 confirmed/fixed 标签且缓存评论没有明确维护者确认；WIP/reported/closed 均不作确认依据。"}]
#5768 Vector FP move/merge instructions missing `frm` reserved value check
https://github.com/OpenXiangShan/XiangShan/issues/5768
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5768", "label_snapshot": "type: bug/confirmed, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5768", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5767 `vlseg2e8ff.v` with later-element fault triggers XiangShan internal critical error
https://github.com/OpenXiangShan/XiangShan/issues/5767
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5767", "label_snapshot": "type: bug/confirmed, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5767", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]

## Slide 19
全量 Issue 清单（11/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
19
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5766 | 2026-04-05 | KnightGOKU | Open | 确认RTL | FOF 后立即读 vl
#5765 | 2026-04-03 | KnightGOKU | Open | 确认RTL | vlm.v mask tail
#5739 | 2026-03-29 | KnightGOKU | Closed | 确认/修复 | vsetvli 后立即读 vl
#5725 | 2026-03-25 | KnightGOKU | Closed | 行为对齐 | reserved vsetvl 对齐
#5702 | 2026-03-19 | biquanha | Closed | 无效报告 | 无效向量访存报告
#5449 | 2025-12-26 | I3eg1nner | Closed | 无效报告 | VectorFloatFMA 对齐
#5426 | 2025-12-24 | cesarus777 | Closed | 确认工具 | NEMU vfredusum
Notes: #5766 `vle8ff` fault-only-first followed by immediate `csrr vl` returns 0 on XiangShan, while Spike returns the expected `vl`
https://github.com/OpenXiangShan/XiangShan/issues/5766
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5766", "label_snapshot": "type: bug/confirmed, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5766", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5765 Difftest mismatch on tail bits of v0 after vlm.v
https://github.com/OpenXiangShan/XiangShan/issues/5765
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5765", "label_snapshot": "type: bug/confirmed, module: backend"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5765", "summary": "GitHub `type: bug/confirmed` 标签；无 tool 标签，按 XiangShan 已确认 RTL/实现问题记录。"}]
#5739 `csrr vl` reads stale zero immediately after `vsetvli`
https://github.com/OpenXiangShan/XiangShan/issues/5739
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5739", "label_snapshot": "module: backend, type: bug/fixed"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5739", "summary": "GitHub `type: bug/fixed` 标签；无 tool 标签，按 XiangShan 已确认且已有修复标签记录。"}]
#5725 Behavior mismatch on RVV testcase (`vsetvl x0, x0, rs2` path)
https://github.com/OpenXiangShan/XiangShan/issues/5725
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5725", "label_snapshot": "module: backend, module: tool, type: bug/fixed"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5725#issuecomment-4132725504", "summary": "维护者 huxuan0307 明确 \"not a bug but a feature\"；后来 NEMU 与 XiangShan 统一对 reserved 情形报非法。", "quote": "Thank you for your bug report. As described in the vector section of the specification, the vsetvl[i] instruction is reserved when rs1 = x0 and rd = x0. Since there is no explicit description of how to implement reserved, the hardware can implement it in any reasonable way. In other words, this is not a bug but a \"feature\".", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5702 Vector memory access
https://github.com/OpenXiangShan/XiangShan/issues/5702
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5702", "label_snapshot": "type: bug/invalid, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5702", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5449 VectorFloatFMA module operation alignment logic error
https://github.com/OpenXiangShan/XiangShan/issues/5449
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5449", "label_snapshot": "type: bug/invalid"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5449", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5426 v31_low different on vfredusum.vs
https://github.com/OpenXiangShan/XiangShan/issues/5426
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5426", "label_snapshot": "module: tool, type: bug/fixed"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5426#issuecomment-3692247360", "summary": "维护者 lewislzh 明确 NEMU bug、\"RTL implementation is correct\"。", "quote": "Thanks for the issue report. This is indeed a bug in the NEMU simulator (the RTL implementation is correct)：\nThe RISC-V Vector specification states that for the vfredusum instruction, when an operand is masked off, it may be treated as -0 if the rounding mode is not RDN; for RDN, the operand needs to be treated as +0. NEMU’s handling of the RDN case was incorrect. A fix has been submitted.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]

## Slide 20
全量 Issue 清单（12/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
20
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#5425 | 2025-12-24 | cesarus777 | Closed | 无效报告 | indexed store assertion
#5424 | 2025-12-24 | cesarus777 | Closed | 工具重复 | DiffTest 重复映射
#5288 | 2025-12-01 | youzi27 | Closed | 无效报告 | 自修改覆盖 fence.i
#5279 | 2025-11-29 | youzi27 | Open | 确认工具 | DiffTest store commit
#4368 | 2025-03-06 | WaltJr-OH | Closed | 讨论/建议 | VLEN 配置讨论
#4190 | 2025-01-16 | camel-cdr | Closed | 确认性能 | 向量吞吐/假依赖
#4017 | 2024-12-10 | jlong299 | Closed | 讨论/建议 | store-load 检查讨论
Notes: #5425 Assertion failed at DCache on vector indexed segment store instructions
https://github.com/OpenXiangShan/XiangShan/issues/5425
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5425", "label_snapshot": "type: bug/invalid, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5425", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5424 Mismatch for store commits on vector indexed segment store instructions
https://github.com/OpenXiangShan/XiangShan/issues/5424
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5424", "label_snapshot": "note: duplicate, module: tool"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5424#issuecomment-3689978534", "summary": "Yan-Muzi：Please refer to #5279", "quote": "Please refer to #5279.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#5288 Unexpected interaction between vs1r.v and fence.i instructions
https://github.com/OpenXiangShan/XiangShan/issues/5288
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5288", "label_snapshot": "type: bug/invalid, module: unknown"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5288", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#5279 Mismatch in vector store commit behavior under misaligned base address
https://github.com/OpenXiangShan/XiangShan/issues/5279
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5279", "label_snapshot": "type: bug/confirmed, module: tool"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/5279#issuecomment-3595092909", "summary": "维护者 Yan-Muzi 明确：\"known bug of difftest\"，非 RTL。", "quote": "It is a known bug of difftest. We have not really figured out how to compare store commits of vector stores. We may fix this in the future.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#4368 Vector Configuration
https://github.com/OpenXiangShan/XiangShan/issues/4368
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4368", "label_snapshot": "type: question/answered"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4368", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#4190 KunminghuV2Config doesn't seem to dual issue vector instructions
https://github.com/OpenXiangShan/XiangShan/issues/4190
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4190", "label_snapshot": "type: bug/reported"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4190#issuecomment-2597589506", "summary": "维护者确认不必要vd依赖性能问题，PR4198修复且报告者回测；LMUL1解码限制另属设计取舍", "quote": "The above issue has been fixed by https://github.com/OpenXiangShan/XiangShan/pull/4198", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#4017 Store-load violation checking for vector instruction
https://github.com/OpenXiangShan/XiangShan/issues/4017
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4017", "label_snapshot": "type: question/answered"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/4017", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]

## Slide 21
全量 Issue 清单（13/13）
“确认/修复”表示已有修复证据；日期均为 UTC；详细依据见本页备注
21
Issue | 创建日期 | 作者 | 状态 | 确认/归属 | 内容
#3962 | 2024-11-29 | H-Y-B | Closed | 讨论/建议 | 关闭 V 扩展配置
#3488 | 2024-09-03 | camel-cdr | Closed | 讨论/建议 | vcompress 优化建议
#3200 | 2024-07-14 | camel-cdr | Closed | 讨论/建议 | RVV benchmark 性能
#3012 | 2024-05-27 | cyyself | Closed | 工具历史 | NEMU 历史修复
#2890 | 2024-04-16 | camel-cdr | Closed | 部分确认 | 长程序/多问题历史
Notes: #3962 How to turn off vector instruction extension？
https://github.com/OpenXiangShan/XiangShan/issues/3962
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3962", "label_snapshot": "type: question/answered"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3962", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#3488 Why does only one execution unit support vppu? & vcompress optimization suggestion
https://github.com/OpenXiangShan/XiangShan/issues/3488
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3488", "label_snapshot": "type: question/answered"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3488", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#3200 rvv-bench: XiangShan performance problems
https://github.com/OpenXiangShan/XiangShan/issues/3200
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3200", "label_snapshot": "type: problem/answered"}, {"kind": "判定", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3200", "summary": "标签为 invalid、已答复问题或 duplicate；关闭本身不构成确认。"}]
#3012 Difftest failed on a RISC-V Vector memcpy workload with misaligned(in vlen granularity, not element) unit stride load
https://github.com/OpenXiangShan/XiangShan/issues/3012
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3012", "label_snapshot": "type: bug/reported"}, {"kind": "最终评论核验", "url": "https://github.com/OpenXiangShan/XiangShan/issues/3012#issuecomment-2134233149", "summary": "作者cyyself：Fixed NEMU commit b9796f4ec8b8427b4fb995ec948ed345f1caeaf4", "quote": "Fixed [https://github.com/OpenXiangShan/NEMU/commit/b9796f4ec8b8427b4fb995ec948ed345f1caeaf4](https://github.com/OpenXiangShan/NEMU/commit/b9796f4ec8b8427b4fb995ec948ed345f1caeaf4) .", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]
#2890 Simulation hangs for longer running functions using the vector extension
https://github.com/OpenXiangShan/XiangShan/issues/2890
[{"kind": "标签", "url": "https://github.com/OpenXiangShan/XiangShan/issues/2890", "label_snapshot": "type: bug/reported"}, {"kind": "最终全评论复核", "url": "https://github.com/OpenXiangShan/XiangShan/issues/2890#issuecomment-2220740793", "summary": "维护者给出RTL修复PR3140/commit1a0c5d且报告者验证；同帖后续还有nexus-am与VS配置问题，不整帖算单一RTL缺陷", "quote": "We have fixed the issue at this commit(1a0c5d77fed8b13a9fa5f70d1f25d808a311dd7b) in this pull requests (https://github.com/OpenXiangShan/XiangShan/pull/3140). This will later be integrated into the master.", "quote_language": "original", "quote_note": "原评论逐行摘录；多行以换行连接，可能省略其他行"}]

## Slide 22
已确认 RTL 问题的代码分组（1）
按目标触发代码与观察点归组，共 28 条，含 1 条重复映射
22
代码形态 | Issue | 共同结构
配置 / CSR | #5739、#6561 | 配置或状态写入后立即观察 CSR
数据 / 标量扩展 | #5829、#5830、#5840、#5928 | 不同位宽、符号位、完整结果读回
mask / tail | #5765 | 先清寄存器，再 load / store mask
非法编码 / 上下文 | #5772、#5809、#5865 | 非法组对齐、vill、vd=v0
合法访存数据 | #5831、#5832、#5932、#5933、#5934 | mixed-EEW、whole、segment

## Slide 23
已确认 RTL 问题的代码分组（2）
按目标触发代码与观察点归组，共 28 条，含 1 条重复映射
23
代码形态 | Issue | 共同结构
FOF | #5766、#5767、#5930、#5931 | 受控 fault 或 active 数据比较
异常地址链 | #5943、#6399、#6482、#6540 | 故障地址与连续异常后状态
访存活性 | #6015、#6022 | 未映射地址和提交进度；含重复
流水队列 | #6467 | 压力前序、inactive store、回绕
静态实现 / 调试 | #5768、#6168 | 有实现代码，未提供完整执行 PoC

## Slide 24
PoC：配置后立即读取 vl
配置与 CSR 组，原帖 #5739 的最小程序
24
li t6, 0x600
csrs mstatus, t6
li a0, 16
vsetvli t1, a0, e8, m1, ta, ma
csrr t2, vl
预期 t1=t2=16，原始故障为 t2=0。
维护者定位 VL bypass 错误并给出修复 PR #5743。
原帖：github.com/OpenXiangShan/XiangShan/issues/5739
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5739。展示原始代码节选，不是独立可运行的完整测试。

## Slide 25
PoC：vl=0 时的 VS 状态副作用
配置与 CSR 组，原帖 #6561 的 failing seed
25
main:
csrwi vcsr, 4
csrwi vstart, 0
vsetivli zero, 0, e64, m1, tu, ma
fmv.x.d s7, fa0
csrrw t2, sstatus, s7
vsseg4e32.v v13, (t6), v0.t
初值 fa0=0xffffffffbf361d42，使 VS=Clean。
本例 vstart=0、vl=0，观察 VS 是否错误变 Dirty，不能忽略 vstart 条件。
原帖：github.com/OpenXiangShan/XiangShan/issues/6561
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/6561。展示原始代码节选，不是独立可运行的完整测试。

## Slide 26
PoC：窄整数移到标量后的符号扩展
数据扩展组，原帖 #5829 的 user_code 节选
26
vsetivli x0, 2, e64, m1, ta, ma
vmv.v.i v9, 0
vsetivli x0, 1, e32, m1, tu, mu
la x10, data_word
vle32.v v9, (x10)
vmv.x.s x15, v9
li x16, 0xffffffffe01d7b92
li gp, 1
beq x15, x16, exit
li gp, 2
data_word 的值为 0xe01d7b92，预期 x15 为其 XLEN 符号扩展。
省略 VS/FS 初始化、trap handler、退出和数据段，其余扩展类按完整目标结果比较。
原帖：github.com/OpenXiangShan/XiangShan/issues/5829
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5829。展示原始代码节选，不是独立可运行的完整测试。

## Slide 27
PoC：mask load 后完整读回
mask / tail 组，原帖 #5765 节选
27
li a0, 16
vsetvli t0, a0, e8, m1, tu, mu
vmv.v.i v0, 0
li a0, 10
vsetvli t0, a0, e8, m1, tu, mu
la a1, mask_data
vlm.v v0, (a1)
la a2, out_data
vsm.v v0, (a2)
mask_data 与 expected_data 均为 .byte 0x80, 0x03。
原程序逐字节比较读回数据，省略初始化、比较循环和 trap handler。
原帖：github.com/OpenXiangShan/XiangShan/issues/5765
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5765。展示原始代码节选，不是独立可运行的完整测试。

## Slide 28
PoC：非法 vtype 后执行向量指令
非法编码 / 上下文组，原帖 #5809 的关键序列
28
vsetvli x21, x21, 992
csrr x23, vl
csrr x22, vtype
vmv.x.s x21, v16
原日志：vl=0，vtype=0x8000000000000000（vill=1）。
预期 mcause=2、mtval=0x43002ad7。原故障却提交了 x21 写回。
原帖：github.com/OpenXiangShan/XiangShan/issues/5809
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5809。展示原始代码节选，不是独立可运行的完整测试。

## Slide 29
PoC：零 stride 的 segment load
合法访存数据组，原帖 #5933 的触发指令节选
29
li x9, 0x8fffffb8
li x10, 0x3803444b2551a2ae
sd x10, 16(x9)
li x10, 0x1000
sd x10, 24(x9)
# ... original intervening instructions omitted ...
li x8, 0x8fffffcd
vlsseg3e64.v v18, (x8), x19
原始触发状态：SEW=64、LMUL=1、x19=0，base 未对齐。
节选保留关键内存写入与目标指令，其余前置代码见原帖，逐 field 比较 active 数据。
原帖：github.com/OpenXiangShan/XiangShan/issues/5933
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5933。展示原始代码节选，不是独立可运行的完整测试。

## Slide 30
PoC：FOF 后立即读取缩短的 vl
FOF 组，原帖 #5766 的 payload 节选
30
li a0, 8
vsetvli t3, a0, e8, m1, tu, mu
vmv.v.i v8, 0
la a1, deny_start
addi a1, a1, -7
vle8ff.v v8, (a1)
csrr t4, vl
la t0, observed_vl
sw t4, 0(t0)
原程序用 PMP 将 deny_start 至 deny_end 设为不可访问。
前 7 字节可访问，第 8 字节 fault：期望读取 vl=7，原报告得到 0。
原帖：github.com/OpenXiangShan/XiangShan/issues/5766
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5766。展示原始代码节选，不是独立可运行的完整测试。

## Slide 31
PoC：FOF segment 的后元素 fault
FOF 组，原帖 #5767 的 payload 节选
31
li a0, 8
vsetvli t3, a0, e8, m1, tu, mu
vmv.v.i v16, 0
vmv.v.i v17, 0
la a2, deny_start
addi a2, a2, -12
vlseg2e8ff.v v16, (a2)
csrr t4, vl
同样使用 PMP deny 区，nf=2，每元素占 2 字节，故障落在后续元素。
原报告触发内部 critical error，期望按 FOF 语义处理。省略 PMP 初始化和 handler。
原帖：github.com/OpenXiangShan/XiangShan/issues/5767
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/5767。展示原始代码节选，不是独立可运行的完整测试。

## Slide 32
PoC：向量异常后的标量异常
连续异常 / fault 地址组，原帖 #6399 的关键序列
32
vsetivli x0, 4, e32, m1, ta, ma
vsse32.v v11, (t4), s1
li a5, 0x0000020000000000
li t2, 0x917af882bf50788e
srl t6, t2, a5
sb sp, -1918(t6)
向量 store 与后续标量 store 依次触发 access fault。
原程序通过 handler 恢复执行，检查第二次 mtval 为本次地址，不能残留第一次地址。
原帖：github.com/OpenXiangShan/XiangShan/issues/6399
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/6399。展示原始代码节选，不是独立可运行的完整测试。

## Slide 33
PoC：未映射地址上的 indexed load 挂死
访存活性组，原帖 #6015 的反汇编摘录
33
80001234: fcvt.d.l fa7, a7
80001238: sha256sum0 s7, a7
8000123c: aes64ds sp, s6, s7
80001240: vluxei32.v v25, (a1), v17
80001244: aes64ks2 s4, s4, a4
a1=0x4ff0b1eb，VL=4，SEW=32，LMUL=1，各索引地址落入未映射区域。
观察异常与提交进度，原报告有 15000 周期无提交。附件提供 ELF，不是汇编源码。
原帖：github.com/OpenXiangShan/XiangShan/issues/6015
Notes: 原帖：github.com/OpenXiangShan/XiangShan/issues/6015。展示原始代码节选，不是独立可运行的完整测试。

## Slide 34
流水队列 PoC：必须保留压力前序
34
#6467 原帖故障指令：vse16.v v10, (t1)，t1=0x80060050。
触发依赖：队列接近回绕、已提交 inactive 项、dataQueue 非空。单独一条 store 不能代表完整复现程序。
原始观察：deqPtr 超过 rdataPtr 的 assertion；禁用 assertion 后出现 store commit 地址 / mask 差异。
维护者确认 deqPtr 更新问题，并说明非对称门控本身是设计选择。附件列出源码与反汇编，此次下载未成功。
Notes: https://github.com/OpenXiangShan/XiangShan/issues/6467
[{"url": "https://github.com/OpenXiangShan/XiangShan/issues/6467#issuecomment-5506320043", "body": "Thanks for your report. We'll look into this.", "user": {"login": "ChrisYzcc", "name": "ChrisYzcc", "email": null, "avatar_url": "https://avatars.githubusercontent.com/u/117955876?v=4", "id": 117955876}, "id": 5506320043, "pull_request_review_id": null, "in_reply_to_id": null, "created_at": null, "updated_at": null, "review": null, "side": null, "line": null, "start_line": null, "path": null, "body_html": "<p dir=\"auto\">Thanks for your report. We'll look into this.</p>"}, {"url": "https://github.com/OpenXiangShan/XiangShan/issues/6467#issuecomment-5522852062", "body": "Thank you for your report! About your question:\n\n1. That's indeed a bug of `deqPtr` update, and it's the first time to be observed.\n2. The asymmetric `dataQueue.io.empty` gate between the `deqPtr` (:1272) and `rdataPtr` (:1302) inactive skips is intentional. We fixed it in #6474\n3. The vector unit of tip is under refactor, it may **can't execute complex vector instruction** (such as **stride** or **index** vector memory instruction) . The bug report base on `68901834` is all right.\n4. You can construct a test case: use a large number of stores with different cache lines to cause `Sbuffer` to have **L1 miss evictions** and then perform inactive vector stores.", "user": {"login": "weidingliu", "name": "weidingliu", "email": null, "avatar_url": "https://avatars.githubusercontent.com/u/47169884?v=4", "id": 47169884}, "id": 5522852062, "pull_request_review_id": null, "in_reply_to_id": null, "created_at": null, "updated_at": null, "review": null, "side": null, "line": null, "start_line": null, "path": null, "body_html": "<p dir=\"auto\">Thank you for your report! About your question:</p>\n<ol dir=\"auto\">\n<li>That's indeed a bug of <code class=\"notranslate\">deqPtr</code> update, and it's the first time to be observed.</li>\n<li>The asymmetric <code class=\"notranslate\">dataQueue.io.empty</code> gate between the <code class=\"notranslate\">deqPtr</code> (:1272) and <code class=\"notranslate\">rdataPtr</code> (:1302) inactive skips is intentional. We fixed it in <a class=\"issue-link js-issue-link\" data-error-text=\"Failed to load title\" data-id=\"5334191581\" data-permission-text=\"Title is private\" data-url=\"https://github.com/OpenXiangShan/XiangShan/issues/6474\" data-hovercard-type=\"pull_request\" data-hovercard-url=\"/OpenXiangShan/XiangShan/pull/6474/hovercard\" href=\"https://github.com/OpenXiangShan/XiangShan/pull/6474\">#6474</a></li>\n<li>The vector unit of tip is under refactor, it may <strong>can't execute complex vector instruction</strong> (such as <strong>stride</strong> or <strong>index</strong> vector memory instruction) . The bug report base on <code class=\"notranslate\">68901834</code> is all right.</li>\n<li>You can construct a test case: use a large number of stores with different cache lines to cause <code class=\"notranslate\">Sbuffer</code> to have <strong>L1 miss evictions</strong> and then perform inactive vector stores.</li>\n</ol>"}]

## Slide 35
静态代码证据：FOF 的 watchpoint 丢失
#6168，维护者确认 known issue；原帖不是完成的汇编 PoC
35
when(!entry.fof || vstart === 0.U){
entry.vstart := vstart
entry.exceptionVec := selExceptionVec
entry.uop.trigger := selPort.trigger // trigger only saved here
entry.vaddr := vaddr
...
}.otherwise{
entry.vl := Mux(entry.vl < vstart, entry.vl, vstart) // trigger lost
}
后元素 FOF 进入 otherwise 分支，仅更新 vl，原报告指出 trigger 未保存。
#5768 同样以 frm 检查的实现条件为证据，二者需要另建执行级测试。
原帖：github.com/OpenXiangShan/XiangShan/issues/6168
Notes: https://github.com/OpenXiangShan/XiangShan/issues/6168

## Slide 36
性能代码单列：LMUL=2 的吞吐测试
#4190 原帖 bench_vaddvv_m2 节选，UNROLL=8，LOOP=64
36
vsetvli t0, x0, e32, m2, ta, ma
li a0, LOOP
csrr a1, cycle
1:
.rept UNROLL
vadd.vv v8,v16,v24
vadd.vv v10,v18,v26
vadd.vv v12,v20,v28
vadd.vv v14,v22,v30
.endr
addi a0, a0, -1
bnez a0, 1b
fence.i
csrr a0, cycle
sub a0, a0, a1
观察 cycle 差值。维护者确认不必要的 vd 依赖并给出 PR #4198，
LMUL=1 的每周期解码限制则是另一项设计取舍。
原帖：github.com/OpenXiangShan/XiangShan/issues/4190
Notes: https://github.com/OpenXiangShan/XiangShan/issues/4190

## Slide 37
PoC 可用性与解释边界
37
完整源码、关键指令节选、反汇编和实现代码分别标注，不能视作同一种证据。
#5772 附件包含 .S 源码；#6015 附件仅有 1 个 ELF；#6482 附件含 98 个 ELF。
#5768 / #6168 只有实现级证据或未完成执行 PoC；#6467 的压力程序附件本次未成功下载。
#2890 混合历史 RTL 修复、nexus-am 与配置问题；#6576 有 v2 修复线索和 v3 移植计划，均不整帖计入严格确认 RTL 数。

## Slide 38
Mutation 建议：围绕触发条件做变异
以下是基于真实 PoC 的测试设计建议，不是已完成的实验结果
38
先保留原始 PoC 的分支、commit、初值、内存布局与 oracle，建立能够稳定运行的基线。
每次改变一个关键维度，并加入相邻合法或无故障对照，再做有约束的组合覆盖。
保留预期非法和内存异常样本，不能只回放 Retire_Success。目标指令后增加 CSR、寄存器或内存观察。
每个变体关联原 Issue；输入不同不等于新的根因。性能、参考模型和 RTL 结果分别统计。

## Slide 39
Mutation：CSR、数据与合法性
39
目标形态 | 优先变异 | 必须保持与观察
配置 / CSR | AVL、SEW、LMUL；CSR 相邻距离 | 保持可执行配置，比较返回 rd 与新 vl
VS 状态副作用 | vl=0/1；vstart=0/非0；Clean/Dirty | 区分是否改变向量状态，再判断 Dirty
数据扩展 / NaN-box | SEW、符号边界、扩展倍率 | 完整标量 / 向量读回，高位必须检查
mask / tail | vl 边界、位图、tu/ta、mu/ma | 先写唯一哨兵，期望遵循具体策略
非法编码 / 上下文 | vill、组对齐、reserved 字段 | 修改字段时保留其他前提，检查 trap

## Slide 40
Mutation：内存、异常与活性
40
目标形态 | 优先变异 | Oracle / 对照
合法 load / store | stride=0/非0，nf、EEW、base 对齐 | 每 lane / field 唯一数据，完整读回
FOF | fault 位于首/后元素；PMP 边界 | vl、部分结果、异常种类，无故障对照
连续 fault | 地址 A/B、load/store 方向、特权级 | mtval/stval 应属于本次 fault
队列 / 活性 | cache-line 压力、inactive 项、回绕 | 提交进度、assertion、commit 地址
调试 / 性能 | watchpoint 与 FOF；依赖与 LMUL | 调试事件独立监测，性能单列 cycle

## Slide 41
建议实施顺序
41
第一阶段：使用已有真实源码，补齐 CSR、标量扩展、mask、非法指令的明确 oracle。
第二阶段：搭建可控内存与 trap handler，按 FOF、segment、连续 fault 的原始结构扩展。
第三阶段：保留压力序列与提交日志，覆盖队列回绕、挂死及调试触发器，性能使用独立预算。
每次输出记录关联 Issue、原始 PoC、变异参数和完整初值，附预期/实际结果及最小化程序。
确认问题与变体分别计数。